# SYSC3601 LABORATORY #1 (Summer 2014) - Home preparation

1) In the program shown below, hand assemble the two instructions whose object code is not shown. Show how each bit of the hand assembled instructions was determined (i.e. show each bit field of the instruction as well as the ultimate hex byte values).

.8086

NAME TEST

;**

;** A simple test program that enters an infinite loop.

;**

PROG	SEGMENT

ORG	00100h

ASSUME CS:PROG,DS:PROG

START:

MOV	CX,CS			__ __

MOV 	DS,CX			8E D9

LOOP1:	MOV	BX,176h		BB 76 01

MOV	AX,[BX+4]		8B 47 04

ADD	AX,[BX+8]		03 47 08

MOV	[BX+6],AX		89 47 06

MOV	BX,180h		BB 80 01

MOV	[BX-2],AX		__ __ __

JMP	LOOP1			EB EC

PROG		ENDS

END	START

Assuming that the contents of memory before the program is run are given below on the left, show the contents of memory immediately after the JMP instruction is executed for the third time. Assume that CS=0000h in the above program.

| Before: 2F 0018Ah 2E 00189h 2D 00188h 2C 00187h 2B 00186h 2A 00185h 1F 00184h 1E 00183h 1D 00182h 1C 00181h 1B 00180h 1A 0017Fh 19 0017Eh 18 0017Dh 17 0017Ch 16 0017Bh 15 0017Ah 14 00179h 13 00178h 12 00177h 11 00176h | After 1st JMP: After 2nd JMP: After 3rd JMP: 0018Ah 0018Ah 0018Ah 00189h 00189h 00189h 00188h 00188h 00188h 00187h 00187h 00187h 00186h 00186h 00186h 00185h 00185h 00185h 00184h 00184h 00184h 00183h 00183h 00183h 00182h 00182h 00182h 00181h 00181h 00181h 00180h 00180h 00180h 0017Fh 0017Fh 0017Fh 0017Eh 0017Eh 0017Eh 0017Dh 0017Dh 0017Dh 0017Ch 0017Ch 0017Ch 0017Bh 0017Bh 0017Bh 0017Ah 0017Ah 0017Ah 00179h 00179h 00179h 00178h 00178h 00178h 00177h 00177h 00177h 00176h 00176h 00176h |
| --- | --- |

2) Assuming that the 8086 is running at 2MHz, in the space below, complete the WAIT subroutine by writing a series of instructions to create a delay of one second. Ignore the times taken by any other code outside of WAIT. Make use of the instruction encoding handout and Appendix B of the Brey text to determine how many clock cycles are taken by each instruction. Note that any registers that are to be modified by this subroutine must be first saved (pushed) on the stack and restored (popped) off the stack at the end of the subroutine (i.e. register contents must be preserved). Please show the number of clocks required for each instruction of your program. You are free to use any 8086 instructions in your subroutine (but not the MASM ‘dot macros’ such as ‘.if’). Note that you will have to find the cycle timing for PUSH and POP in the text or on the web.

CPU is running at 2MHz or ___________ cycles/second.

Therefore 1 clock (cycle) will cause a delay of __________  seconds.

If the WAIT subroutine has a loop that executes ___________ times (<= 64K),

then each loop must have approx _________ cycles.

The total time for my WAIT subroutine is: _________ cycles, or ________ ms

;** WAIT ** (Please write code below in space provided).

;**

;** Contains loop(s) which run for approximately one second (within 25%).

;**

;** Remember to show the number of cycles required for each instruction

| Label | Instruction | Cycles per execution | Times executed | Total cycles |
| --- | --- | --- | --- | --- |
| WAIT | PROC NEAR |  |  |  |
|  | RET |  |  |  |
| WAIT | ENDP |  |  |  |

# Text boxes

MOV CX,CS bit field details:

MOV [BX-2],AX bit field details: