## Slide 1: Fundamentals of Cellular Communications and Networks
Halim Yanikomeroglu
SYSC 4700
Lectures 15 (March 06) & 16 (March 08)

## Slide 2: Objectives
  To learn some fundamental concepts in cellular communications such as
    Multiple access
    Channel reuse
    Clustering
    Cell-splitting
    Sectoring
    Interference
    Duplexing
    Heterogeneous cellular network

## Slide 3: Multiple Access Schemes
  Dedicated medium vs shared medium
  Shared Medium
  Random access (minimal protocol, no or minimal coordination)
  No or limited QoS guarantee
  Suitable for unlicensed bands
    ALOHA
    CSMA (carrier sense multiple access), aka listen-before-talk – used in WiFi (802.11)

## Slide 4: Multiple Access Schemes
  Dedicated medium vs shared medium
  Shared Medium
  Random access (minimal protocol, no or minimal coordination)
  No or limited QoS guarantee
  Suitable for unlicensed bands
    ALOHA
    CSMA (carrier sense multiple access), aka listen-before-talk – used in WiFi (802.11)
  Scheduled access (protocol for coordination  overhead)
  QoS quarantee
  Suitable for licensed bands
    TDMA (time-division multiple access)
    FDMA (frequency-division multiple access), OFDMA – used in 4G cellular
    CDMA (code-division multiple access) – used in 3G cellular

## Slide 7
Wireless Cellular Networks

## Slide 8
Wireless Cellular Networks
Handoff  Seamless roaming
Network-wide managing channel reuse
through network-wide frequency (channel) planning
 Quality-of-Service (QoS) guarantee

## Slide 9: Wireless access
  Through access points (base stations), coupled to the wired (core) network
  Attain coverage with minimum infrastructure cost
    Put as few base stations as possible

## Slide 10: Channel Reuse (1/3)
Problem: Number of channels << number of active users!
  Ex: # of users (subscribers) = 200,000 Percentage of active users = 5% # number of active users = 10,000 BW leased = 10 MHz BW required per user = 25 KHz
  400 << 10,000 !!!
  How can you service 10,000 users with only 400 channels?
Answer: Reuse the channels (radio resources)
# available channels = 10 MHz/ 25 KHz = 400

## Slide 11: Channel Reuse (2/3)
A naïve approach in RAN (Radio Access Network) design:
  1 BS (1 cell) gives service to all 10,000 active users
  Each of the 400 channels is reused 25 times in the one-cell network (400 x 25 = 10,000)
  SIR = (1 good signal)/(24 interfering signals) = 1/24 = -14 dB!
  Extremely unreliable channel  No application will run…
Refine RAN (i.e., more infrastructure + protocol + complexity for enhanced performance)

## Slide 12: Channel Reuse (3/3)
  Channel (frequency, time, code, hybrid) reuse in a coordinated manner  cellular concept
  Ex: 25 reuses in non-overlapping areas (clusters). Each cluster is given service by 1 BS (cell)
  Cluster: The area in which all the channels are used only once.

## Slide 13: Interference due to Channel Reuse
  Problem: If two users in adjacent clusters are served through the same channel i (one channel out of 400), then there will be excessive multiple access interference!
  SIR = 1/1 = 0 dB (very low)
  Multiple access interference: Inevitable in cellular systems, but can be regulated
  Control and management of multiple access interference:
    Radio resource management (RRM)
    Optimization of assignment problems
      BS/AP assignment
      Power assignment
      Channel assignment

## Slide 14: Regulating Channel Assignment (1/2)
  Divide each cluster into cells (cell: area served by one base station)
4 cells/cluster
Cluster size: N=4
Reuse factor = 1/N = 1/4
A: ch 1 to 100
B: ch 101 to 200
C: ch 201 to 300
D: ch 301 to 400

## Slide 15: Regulating Channel Assignment (2/2)
  Cluster size N
    N↑ → co-channel interference (CCI) ↓  SIR ↓
    N↑ → capacity/cell decreases (inefficient utilization of the infrastructure, this, the investment)
  Example (400 channels per cluster):
A | B | A | B
C | D | C | D
A | B | A | B
C | D | C | D
A | B | A | B
A | B | A | B
A | B | A | B
A | B | A | B
Cluster size: N=4
# channels per cell = 100
Cluster size: N=2
# channels per cell = 200

## Slide 16: Cluster size and Quality of Service (1/2)
  Ex: Signal-to-Interference Ratio (SIR) calculation with N=4
The marked two users in Cell A and Cell A’ use the same transmit power Pt
Uplink with

## Slide 17: Cluster size and Quality of Service (2/2)
  Ex: SIR calculation with N=9
  - Example: # cells = 100, # channels = k
  N=4  Network capacity = # clusters * k = (100/4) k = 25k
  N=5  Network capacity = # clusters * k = (100/5) k = 20k
    N↑ → co-channel interference↓ → QoS (SIR) ↑
    But, for the same number of Base Stations,
    N↑ → # clusters ↓ → network capacity ↓

## Slide 18: Increased user demand
  Demand ↑ → more reuse → # clusters ↑
  If cluster size remains the same → more cells in the same area → Cell splitting

## Slide 19: Mobility
  Handoff (handover): Seamless transition

## Slide 20: Coverage region of a base station
  Propagation on a flat terrain (no shadowing)
  With shadowing
  Non-uniform demand

## Slide 21: Hexagonal Layout

## Slide 22: Sectoring
Use directional antenna to reduce co-channel interference, thus we can use small cluster size → increase capacity
  Wireless Communications: Principles and Practice, 2nd Edition by T.S. Rappaport
120 degree antennas
are the most popular
Better SIR,
More capacity
But
More handoff
More antennas and their RF’s parts

## Slide 23: Duplexing
Duplexing: Decoupling the uplink and downlink
Frequency division duplexing (FDD): requires paired spectrum
Time division duplexing (TDD): a single block of spectrum is sufficient

## Slide 24: Types of Interference

## Slide 25: HetNet: Heterogeneous Wireless Network
HetNet
Relay
Relay
CoMP
CoMP

## Slide 26: Question
Goal: To provide a cellular voice service to a town using 20 MHz of bandwidth; each user requires 20 kHz of bandwidth for voice communications.
How many users can be supported concurrently, using a single high power transmitter to cover the whole town?
20 MHz / 20 KHz = 1,000 users
How many users can be supported concurrently, using a cellular topology with 20 base stations and a cluster size of 4?
  Divide the 20 MHz BW into 4 sets and assign one set to each cell
  Each cell has a BW of 20 (MHz/cluster) / 4 (cells/cluster) = 5 MHz/cell
  # of users per cell = 5 (MHz/cell) / 20 (kHz/user) = 250 users/cell
  The total number of users = 250 users/cell * 20 cells = 5,000 users