## Slide 1
5G and Beyond Wireless Networks:
Emerging Concepts and Technologies
Halim Yanıkömeroğlu
Carleton University
Ottawa, Canada

## Slide 2: Carleton University
Ottawa, Canada
Est. in 1946
30,000 students
Engineering
Notes: 2

## Slide 3: 5G Discussions – Everywhere…
Globecom 2017 Industry Seminars
5G & Beyond Research through Industry-University Collaboration
V2X for Automated Driving in 4G, 5G and beyond
5G Heterogeneous and Small Cell Networks (HetSNets)
Towards 5G Internet-of-Things – URLLC in Automotive and Industrial IoT Applications
Globecom 2017 Industry Panels
5G Use Cases, Services and Applications: Reality, Prospects and Challenges
Multi SDOs/For a Industry Harmonization … and 5G SW PoCs
Accelerate 5G Adoption in Enterprises and Verticals: Learnings, Pitfalls, and Controversies
5G Vision to Reality: 5G Commercialization – New Services and Business Opportunities
5G Vision to Reality: Technical Challenges in Early 5G Commercialization and Advanced Technologies for 5G Evolution
Role of Licensed and Unlicensed Millimeter Wave in Delivering the Promise of 5G
5G Today and 5G Tomorrow: Technology Trends Shaping the Evolution of 5G
Future Indoor Communications: Requirements and Challenges on the Path towards 5G
Abundant material online

## Slide 4: Why this Tutorial? – What to Expect / What not to Expect

## Slide 5: Why this Tutorial? – What to Expect / What not to Expect
Not about the standards details
Not a marketing pitch
Not wild predictions

## Slide 6: Why this Tutorial? – What to Expect / What not to Expect
Not about the standards details
Not a marketing pitch
Not wild predictions
An academic’s perspective
partly factual, partly opinionated, partly guesswork
Diverse set of topics: Systems view (no one knows all of it)
Relevance to 4G/5G/6G and even beyond

## Slide 7
Technologies for the Wireless Future
Wireless World Research Forum (WWRF), 2006
The key technological vision from WWRF is
“7 trillion wireless devices serving 7 billion people
It is Difficult to Guess the Future

## Slide 8
Technologies for the Wireless Future
Wireless World Research Forum (WWRF), 2006
The key technological vision from WWRF is
“7 trillion wireless devices serving 7 billion people by 2017”
It is Difficult to Guess the Future

## Slide 9: Engineering Design Methodology
Architecture, enablers, technologies
(5G and beyond)
Part I
Part II
Technical requirements (5G)
Use cases (5G)
Part III

## Slide 10: Part I: Use Cases (~80 slides)
Generations of cellular technologies (1G  4G)
3GPP
5G: A game changer
ICT
Concluding remarks

## Slide 11: Part II: Technical Requirements (~70 slides)
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks

## Slide 12
Problem Statement and Solution Guidelines
HetHetNets: 5G+ Traffic Models
Ultra-Agile Networks for Wireless Ultra-Connectivity
  Spectrum
  Aerial BSs (Non-Terrestrial Networks
  User-in-the-Loop (UIL: Demand Shaping in Space & Time)
  Advanced PHY
    Optimized PHY with Massive Look-Up Tables
    Non-Coherent Communications
    Faster-Than-Nyquist Signaling
Concluding Remarks
Part III: Ultra-Agile Networks for Wireless Ultra-Connectivity (~250 slides)

## Slide 13: Part I: Use Cases
Generations of cellular technologies (1G  4G)
3GPP
5G: A game changer
ICT
Concluding remarks

## Slide 14
Wireless Cellular Networks

## Slide 15
Wireless Cellular Networks
Handoff  Seamless roaming
Network-wide frequency (channel) planning  Quality-of-Service (QoS) guarantee

## Slide 16: Mobile phone (1946)

## Slide 17: Mobile phone  Cell phone

## Slide 18
Mobile phone  Cell phone  Smart phone  Tablets

## Slide 19
Evolution of Use-Cases in Cellular from 1G to 4G
voice
text, email, browsing
video

## Slide 20: Cisco Visual Networking Index: Global Mobile Data Traffic Forecast

## Slide 21
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast

## Slide 22
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast

## Slide 23
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast

## Slide 24: Near Future: More Video

## Slide 25: What is 5G?
5G is not about only smart phones
Notes: 25

## Slide 26: What is 5G?
5G is about novel use cases
5G is not about only smart phones
Notes: 26

## Slide 27: 5G Use Cases
A. Dutta, AT&T
Notes: 27

## Slide 28: Problem with 5G Discussions
1G– 4G discussions: All around phone
5G: Too many very different use cases with one discussion
Challenges, required technologies, and market demand are very different

## Slide 29: Part I: Use Cases
Generations of cellular technologies (1G  4G)
3GPP
5G: A game changer
ICT
Concluding remarks

## Slide 30: Patents are Important
Qualcomm royalty fee: $16.25 per 5G smart phone
2.275%  5% of the selling price (up to $500)
Ericsson royalty fee: $5 per 5G smart phone

## Slide 31: Patents are Important
Nortel’s patents were sold in June 2011 to a consortium consisting of Apple, Ericsson, Microsoft, Blackberry and Sony.
6,000 patents for $4.5 B  $750,000 per patent

## Slide 32: Companies with the Highest Number of Issued US Patents in 2014
IBM USA 7,534
Samsung S. Korea 4,952
Canon Japan 4,055
Sony Japan 3,224
Microsoft USA 2,829
Toshiba Japan 2,608
Qualcomm USA 2,590
Google USA 2,566

## Slide 33
Generations of Cellular Networks
0G: Non-cellular mobile 1G: AMPS, 1983 2G: GSM, 1991

## Slide 34
Generations of Cellular Networks
0G: Non-cellular mobile 1G: AMPS, 1983 2G: GSM, 1991
3GPP Platform: [Est. 1998] “unites 6 telecom standard development organizations (ARIB, ATIS, CCSA, ETSI, TTA, TTC), and provides their members with a stable environment to produce the highly successful Reports and Specifications that define 3GPP technologies”. (Other platforms and organizations: 3GPP2, IEEE, …)

## Slide 35
2011
2010
2009
2008
2007
2006
2005
2004
2003
2002
2001
2000
R99
R4
R5
R6
R7
R8
R9
R10
2012
R11
Release 13: Mar 2016
Release 14: Jun 2017
2013
2014
2015
R12
Generations of Cellular Networks
0G: Non-cellular mobile 1G: AMPS, 1983 2G: GSM, 1991
3GPP Platform

## Slide 36
2011
2010
2009
2008
2007
2006
2005
2004
2003
2002
2001
2000
R99
R4
R5
R6
R7
R8
R9
R10
2012
R11
Release 13: Mar 2016
Release 14: Jun 2017
2013
ITU-R IMT-2000 circular letter ITU-R IMT-Advanced circular letter
3GPP Platform
2014
2015
R12
Generations of Cellular Networks
0G: Non-cellular mobile 1G: AMPS, 1983 2G: GSM, 1991
1 Gbps hotspot / 100 Mbps mobile
2 Mbps mobile

## Slide 37
2011
2010
2009
2008
2007
2006
2005
2004
2003
2002
2001
2000
R99
R4
R5
R6
R7
R8
R9
R10
UMTS
HSPA
DL
HSPA
UL
LTE
LTE
Adv
HSPA+
2012
R11
Release 13: Mar 2016
Release 14: Jun 2017
2013
ITU-R IMT-2000 circular letter ITU-R IMT-Advanced circular letter
3GPP Platform
2014
2015
R12
Generations of Cellular Networks
0G: Non-cellular mobile 1G: AMPS, 1983 2G: GSM, 1991
1 Gbps hotspot / 100 Mbps mobile
2 Mbps mobile

## Slide 38
2011
2010
2009
2008
2007
2006
2005
2004
2003
2002
2001
2000
R99
R4
R5
R6
R7
R8
R9
R10
UMTS
HSPA
DL
HSPA
UL
LTE
LTE
Adv
HSPA+
2012
R11
Release 13: Mar 2016
Release 14: Jun 2017
3G: IMT-2000 compliant 4G: IMT-Advanced compliant
2013
ITU-R IMT-2000 circular letter ITU-R IMT-Advanced circular letter
2014
2015
R12
Generations of Cellular Networks
0G: Non-cellular mobile 1G: AMPS, 1983 2G: GSM, 1991
1 Gbps hotspot / 100 Mbps mobile
2 Mbps mobile
3GPP Platform

## Slide 39
LPWA (Low-Power Wide-Area):
Utility meters, street lights, pet or personal asset trackers, etc.
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast

## Slide 40
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast

## Slide 41: Part I: Use Cases
Generations of cellular technologies (1G  4G)
3GPP
5G: A game changer
ICT
Concluding remarks

## Slide 42
1G
2G
3G
4G
Mbps
kbps
bps
Mbps
kbps
bps
Gbps
2020
2010
2000
1990
1980
AMPS
AMPS
Mobile device for everyone
Time
data
data
data
Cellular Generations – 1G, 2G, 3G, 4G
Notes: 42
2010 – 20 - will be the decade of LTE
2020 -> - will be 5th G what will it hold?
Not entirely sure but – what is sure is that Between Now and then-
Cell size will definitely shrink – and consequently
Cell count will increase
All in an order of magnitude
Devices will undoubtedly expand exponentially
Data M2M will explode – And this will inevitably lead to a concatenation of growth trends
The growing need for information and interaction will spur a number of Mega-trends ……

## Slide 43
1G
2G
3G
4G
5G
Mbps
kbps
bps
Mbps
kbps
bps
Gbps
2020
2010
2000
1990
1980
AMPS
?
AMPS
?
Mobile device for everyone
Time
Cellular Generations – 2010 View
data
data
data
data
Notes: 43
2010 – 20 - will be the decade of LTE
2020 -> - will be 5th G what will it hold?
Not entirely sure but – what is sure is that Between Now and then-
Cell size will definitely shrink – and consequently
Cell count will increase
All in an order of magnitude
Devices will undoubtedly expand exponentially
Data M2M will explode – And this will inevitably lead to a concatenation of growth trends
The growing need for information and interaction will spur a number of Mega-trends ……

## Slide 44
1G
2G
3G
4G
5G
Mbps
kbps
bps
Mbps
kbps
bps
Gbps
2020
2010
2000
1990
1980
AMPS
?
AMPS
?
Mobile device for everyone
Time
Cellular Generations – Current View
data
data
data
data
Notes: 44
2010 – 20 - will be the decade of LTE
2020 -> - will be 5th G what will it hold?
Not entirely sure but – what is sure is that Between Now and then-
Cell size will definitely shrink – and consequently
Cell count will increase
All in an order of magnitude
Devices will undoubtedly expand exponentially
Data M2M will explode – And this will inevitably lead to a concatenation of growth trends
The growing need for information and interaction will spur a number of Mega-trends ……

## Slide 45: Cellular Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
1G
2G
2.5G
3G
3.5G
4G
4.5G
5G
voice

## Slide 46: Cellular Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
1G
2G
2.5G
3G
3.5G
4G
4.5G
5G
voice
data (video)

## Slide 47: Cellular Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
1G
2G
2.5G
3G
3.5G
4G
4.5G
5G
voice
data (video)
novel use-cases

## Slide 48: Cellular Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
1G
2G
2.5G
3G
3.5G
4G
4.5G
5G
voice
data (video)
novel use-cases
novel use-cases:
autonomous & connected vehicles,
IoT, smart grid, smart cities,
smart homes, health care,
remote robotics, tactile internet, …
very many, difficult to list

## Slide 49: Cellular Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
1G
2G
2.5G
3G
3.5G
4G
4.5G
5G
voice
data (video)
novel use-cases
novel use-cases:
autonomous & connected vehicles,
IoT, smart grid, smart cities,
smart homes, health care,
remote robotics, tactile internet, …
very many, difficult to list

## Slide 50: Cellular Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
1G
2G
2.5G
3G
3.5G
4G
4.5G
5G
voice
data (video)
novel use-cases
novel use-cases:
autonomous & connected vehicles,
IoT, smart grid, smart cities,
smart homes, health care,
remote robotics, tactile internet, …
very many, difficult to list
Some of the envisioned use cases will have to wait for the 5G evolution,
or even 6G, or even beyond!

## Slide 51: Direction 1: Enhanced Mobile Broadband (EMBB)

## Slide 52: Direction 2: Massive Machine-Type Communications (MMTC)
IoT
Internet
of Things
IoE
Internet
of Everything
Notes: ITU-T Rec. Y.2221 (www.itu.int/rec/T-REC-Y.2221-201001-I): Requirements for support of Ubiquitous Sensor Network* applications and services.
* This is the ITU-T term for MTC systems and applications involving possible large numbers of sensors potentially spread over a large area
Sensor Networks monitor physical or environmental conditions, (e.g., temperature, sound, vibration, pressure, motion or pollutants) at various locations. These sensors need to communicate with a server.
Early sensor networks operate in isolation. Networked sensor applications enable new possibilities for consumers, public organizations, enterprises, government, etc.
Applications integrate data from sensor networks to achieve industrial or home automation control, agricultural monitoring, healthcare, environment and pollution monitoring, and disaster surveillance, security, etc.

## Slide 53: Direction 3: Mission Critical / Ultra-Reliable Low-Latency Communications (URLLC)
The Ultras

## Slide 54: 5G Requirements
5G hypercube
Notes: 54

## Slide 56: 5G Use Cases Taxonomy
A. Dutta, AT&T

## Slide 57: Detailed Timeline & Process for IMT-2020 in ITU-R
In early 2012, ITU-R embarked on a programme (lead by Working Party 5D) to develop “IMT for 2020 and beyond”, setting the stage for “5G” research activities.

## Slide 58: Detailed Timeline & Process for IMT-2020 in ITU-R
In early 2012, ITU-R embarked on a programme (lead by Working Party 5D) to develop “IMT for 2020 and beyond”, setting the stage for “5G” research activities.
Will a similar process start in 2021 for 6G?

## Slide 59: Detailed Timeline & Process for IMT-2020 in ITU-R
Steps in radio interface development process:
Step1 and 2
No.27
No.28
No.29
No.30
No.31
No.32
No.33
No.34
No.35
Step 3
(0)
(1)
(40 months: #23 - #32)
Step 4
(20 months: #28 - #32)
(16 months: #31 - #34)
(2)
Steps 5, 6, and 7
(3)
Steps 8
(4)
(12 months: #33 - #36)
(28 months: #29 - #35)
WP 5D meetings
Step 1: Issuance of the circular letter
Step 2: Development of candidate RITs and SRITs
Step 3:
Submission/Reception of the RIT and SRIT proposals and acknowledgement of receipt
Evaluation of candidate RITs and SRITs by Independent Evaluation Groups
Step 5:
Review and coordination of outside evaluation activities
Step 6:
Review to assess compliance with minimum requirements
Step 7:
Consideration of evaluation results, consensus building and decision
Step 8:
Development of radio interface Recommendation(s)
Critical milestones in radio interface development process:
(0): Issue an invitation to propose RITs
March 2016
(1): ITU proposed cut off for submission
July 2019
(2): Cut off for evaluation report to ITU
February 2020
(3): WP 5D decides framework and key
June 2020
characteristics of IMT-2020 RIT and SRIT
-
(4): WP 5D completes development of radio
October 2020
interface specification Recommendations
2016
No.36
IMT-2020 2-01
Step 4:
of candidate RIT and SRIT proposals
No.26
No.24
No.25
No.23
2017
2018
2019
2020
ITU-R IMT.2020 Contribution 2
29 June 2016

## Slide 60: 3GPP Timeline

## Slide 61: 5G Eco-system Timeline
Notes: 61

## Slide 62: Current Situation
MMTC: Release-13 NB-IoT (Narrowband IoT)
EMBB: Release-15 NR (New Radio)
URLLC: Release-16 and 5G+

## Slide 63: Cellular/Wireless Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
2030
2025
2035
4G
2040
2045

## Slide 64: Cellular/Wireless Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
2030
2025
2035
1G
2G
3G
4G
5G
6G
2040
2045

## Slide 65: Cellular/Wireless Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
2030
2025
2035
1G
2G
3G
4G
5G
6G
2040
2045
mobile phone
novel use-cases

## Slide 66: Cellular/Wireless Generations: Use-Cases & Timeline
1980
1985
1990
1995
2000
2005
2015
2020
2010
2030
2025
2035
1G
2G
3G
4G
5G
6G
2040
2045
mobile phone
novel use-cases
Wireless 2.0
Wireless ultra-connectivity

## Slide 67: Part I: Use Cases
Generations of cellular technologies (1G  4G)
3GPP
5G: A game changer
ICT
Concluding remarks

## Slide 68: Access to Information
Books
Brick library
Notes: 68

## Slide 69
Books
Brick library
Internet library
Access to Information
Notes: 69

## Slide 70
Books
Brick library
Internet library
Data of all sorts
Access to Information
Notes: 70

## Slide 71
Books
Brick library
Internet library
Data of all sorts
Easy access (I/F)
Access to Information
Notes: 71

## Slide 72
Books
Brick library
Internet library
Data of all sorts
Easy access (I/F)
Available before you ask/think
Access to Information
Notes: 72

## Slide 73
ICT – Information and Communication Technologies
Alan Turing
1912 – 1954
Claude Shannon
1916 – 2001
Communications
Computing
ICT

## Slide 74
ICT – Information and Communication Technologies
Alan Turing
1912 – 1954
Claude Shannon
1916 – 2001
Communications
Computing
ICT
Content

## Slide 75
ICT – Information and Communication Technologies
Alan Turing
1912 – 1954
Claude Shannon
1916 – 2001
Communications
Computing
ICT
Content
S. Andreev, O. Galinina, A. Pyattaev, J. Hosek,
P. Masek, H. Yanikomeroglu, Y. Koucheryavy,
“Exploring synergy between communications,
caching, and computing in 5G-grade
deployments”, IEEE Commun. Magazine, August 2016.

## Slide 76: ICT: Becoming World’s Biggest Industry
ICT: Already ~5% of the global GDP

## Slide 77
iPod
Blackberry
Netbook
iPhone
iPad (2010)
360
300
180
74
28
Number of Days to Reach 1 Million Units Sold
iPad2 (2011)
3

## Slide 78
iPod
Blackberry
Netbook
iPhone
iPad (2010)
360
300
180
74
28
Number of Days to Reach 1 Million Units Sold
iPhone 5: 9 M during launch weekend (20-22 Sept 2013)
iPad2 (2011)
3

## Slide 79
Number of Days to Reach 1 Million Units Sold
iPhone 6: 10 M during launch weekend (19-21 Sept 2014)
Apple Store, 59th Street & 5th Avenue, New York, 05 Sept 2014

## Slide 80
Number of Days to Reach 1 Million Units Sold
iPhone 6s & Plus: 13M during launch weekend (25-27 Sept 2015)
Apple Store, 59th Street & 5th Avenue, New York, 05 Sept 2014

## Slide 81: ICT: Becoming World’s Biggest Industry
ICT: Already ~5% of the global GDP
Cisco Consulting Services 2014 white paper:
IoT: $19 trillion opportunity over the next decade
Will soon become world’s largest industry sector – by far!

## Slide 82: ICT Sector – Unprecedented Value
Market cap Employees Value/employee
Apple $878 B 116,000 $7.6 M 1976
Alphabet $707 B 79,000 $8.9 M 1998
Microsoft $650 B 124,000 $5.2 M 1975
Amazon $560 B 542,000 $1.0 M 1994
Facebook $509 B 21,000 $24.2 M 2004

## Slide 83: ICT Sector – Unprecedented Value
Market cap Employees Value/employee
Apple $878 B 116,000 $7.6 M 1976
Alphabet $707 B 79,000 $8.9 M 1998
Microsoft $650 B 124,000 $5.2 M 1975
Amazon $560 B 542,000 $1.0 M 1994
Facebook $509 B 21,000 $24.2 M 2004
WhatsApp $22 B 55 $400 M 2009

## Slide 84: ICT Sector – Unprecedented Value
Market cap Employees Value/employee
Apple $878 B 116,000 $7.6 M 1976
Alphabet $707 B 79,000 $8.9 M 1998
Microsoft $650 B 124,000 $5.2 M 1975
Amazon $560 B 542,000 $1.0 M 1994
Facebook $509 B 21,000 $24.2 M 2004
WhatsApp $22 B 55 $400 M 2009
S. Aramco ~$2 T

## Slide 85: ICT Sector – Unprecedented Value
Market cap Employees Value/employee
Apple $878 B 116,000 $7.6 M 1976
Alphabet $707 B 79,000 $8.9 M 1998
Microsoft $650 B 124,000 $5.2 M 1975
Amazon $560 B 542,000 $1.0 M 1994
Facebook $509 B 21,000 $24.2 M 2004
WhatsApp $22 B 55 $400 M 2009
S. Aramco ~$2 T
Several ICT companies will be more
valuable than S. Aramco in the next decade

## Slide 86: Forbes 2015 Newcomers
Travis Kalanick
Net worth: $5.3 B
Source of wealth: Uber
(car service)
Kim Bum-Soo
Net worth: $2.9 B
Source of wealth: KakaoTalk
(mobile chat service)
Brian Chesky
Net worth: $1.9 B
Source of wealth: Airbnb
Evan Spiegel and Bobby Murphy
Net worth: $1.5 B each
Source of wealth: Snapchat
Markus "Notch" Persson
Net worth: $1.3 B
Source of wealth: Minecraft
(video game)
Notes: 86

## Slide 87: iCar  What is Next?
Nothing will be the same again

## Slide 88: Part I: Use Cases
Generations of cellular technologies (1G  4G)
3GPP
5G: A game changer
ICT
Concluding remarks

## Slide 89: 5G Ecosystem: Big!
Standards, Fora
Vendors
Operators
Research
Vertical Industries
New Players
Research
Policy

## Slide 90: Today: ICT is an Important Sector
Entertainment
Agriculture
Hospitality
Transportation
Automotive
Health
Municipalities
Energy
Education
Defence
Public Safety
ICT (4G,…)

## Slide 91: Tomorrow: ICT is the Most Important Sector in Digital Economy
ICT (5G,…)
Entertainment
Agriculture
Hospitality
Transportation
Automotive
Health
Municipalities
Energy
Education
Defence
Public Safety
Telecom
 ICT
 Vertical Industries

## Slide 92: Eventually: ICT is the Only Sector in Digital Economy
Defence
Public Safety
Education
Agriculture
Energy
Health
Entertainment
Transportation
Automotive
Municipalities
ICT (W2.0,…)
W2.0: Wireless
ultra-connectivity
is at the heart of ICT

## Slide 93: Part II: Technical Requirements
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks

## Slide 94: From 4G to 5G (1/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)

## Slide 95: Key Technologies for LTE/LTE-Advanced (R8, R9, R10)
OFDM
MIMO
Spectrum aggregation
HetNet, Relay [to be matured]
CoMP (coordinated multipoint) [moved to R11]
 A number of LTE/LTE-A technologies were ahead of their time
DL: 1 Gbps hotspot / 100 Mbps mobile

## Slide 96: From 4G to 5G (2/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)

## Slide 97: R12 Enhancements (June 2011 – March 2015)
Public safety and critical communications, D2D
Group communications
MTC
UE power consumption, small data
Optimized offloading to WLAN

## Slide 98: R13 Enhancements (Sep 2012 – Mar 2016)
LTE in Unlicensed (U-LTE) [LAA (Licensed-Assisted Aggregation)]
Carrier aggregation enhancements (up to 32 CCs)
Enhancements for MTC (high path-loss tolerance)
Enhanced multiuser transmission techniques
Elevation beamforming / Full-dimension MIMO
8  64 antenna ports
Enhancements for D2D
Indoor positioning
Single-cell point-to-multipoint
http://www.3gpp.org/news-events/3gpp-news/1628-rel13
Nokia white paper

## Slide 99: From 4G to 5G (3/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)
3) 5G brainstorming (2012 – 2015)

## Slide 100: 5G Brainstorming in EU
EU Framework Program 7 Call 8 projects (2012 – 2015)
METIS (2012 – 2015): https://www.metis2020.com/documents
EU Framework Program 8, Horizon 2020 (2014 – 2020)
METIS II (July 2015 – June 2017)
5G PPP – The 5G Infrastructure Public Private Partnership (2014)

## Slide 101: From 4G to 5G (4/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)
3) 5G brainstorming (2012 – 2015)
4) 5G spectrum: ITU WRC-15 (Nov 2015, Geneva); ITU WRC-19

## Slide 102: 5G Spectrum
WRC 2019
“Study additional bands above 6 GHz for expanded mobile broadband capacity, setting the stage for the next generation of wireless networks”.
“Will also consider spectrum allocations for High-Altitude Platform Systems, which will enable lower-cost delivery of bandwidth for developing economies and remote areas around the globe”.

## Slide 103: From 4G to 5G (5/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)
3) 5G brainstorming (2012 – 2015)
4) 5G spectrum: ITU WRC-15 (Nov 2015, Geneva); ITU WRC-19
5) 5G definition: ITU circular letter, IMT-2020 (2016)

## Slide 104: From 4G to 5G (6/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)
3) 5G brainstorming (2012 – 2015)
4) 5G spectrum: ITU WRC-15 (Nov 2015, Geneva); ITU WRC-19
5) 5G definition: ITU circular letter, IMT-2020 (2016)
6) 5G standard development: R14 (2017), R15 (2018), R16 (2019)

## Slide 105: R14 Enhancements (March 2016 – June 2017)
Mission critical enhancements
V2x support
eLAA
4 band carrier aggregation
http://www.3gpp.org/release-14

## Slide 106: 5G Standard Development
R14: June 2017
R15: H2 2018
R16: Dec 2019
RAN 5G Workshop , 18-19 Sep 2015 – “The Start of Something”
Enhanced Mobile Broadband
Massive Machine Type Communications
Ultra-reliable and Low-Latency Communications

## Slide 107: From 4G to 5G (7/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)
3) 5G brainstorming (2012 – 2015)
4) 5G spectrum: ITU WRC-15 (Nov 2015, Geneva); ITU WRC-19
5) 5G definition: ITU circular letter, IMT-2020 (2016)
6) 5G standard development: R14 (2017), R15 (2018), R16 (2019)
7) 5G standard approval (~2020)

## Slide 108: From 4G to 5G (8/8)
1) 4G: R8 LTE (2009), R9 (2010), R10 LTE-A (2011)
2) 4G clean-up + new use-cases: R11 (2013), R12 (2015), R13 (2016)
3) 5G brainstorming (2012 – 2015)
4) 5G spectrum: ITU WRC-15 (Nov 2015, Geneva); ITU WRC-19
5) 5G definition: ITU circular letter, IMT-2020 (2016)
6) 5G standard development: R14 (2017), R15 (2018), R16 (2019)
7) 5G standard approval (~2020)
8) 5G evolution (2020–2030): R17, …

## Slide 109
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks
Part II: Technical Requirements

## Slide 110: Peak Data Rates in the Next 30 Years
1990 – 2020: Kbps  Gbps
2020 – 2050: Gbps  Pbps ?

## Slide 111: Gbps Wireless  Tbps (1012) Wireless  Pbps (1015) Wireless ?
Fundamental dynamics: 3 + 1 rule
BS capacity
  Bandwidth: W
  Received power: Ps
  Min # of antennas: n
RBS = n x W x log(1+SNR) = n x W x log(1+Ps /nWN0)
}
Notes: 111

## Slide 112: Gbps Wireless  Tbps (1012) Wireless  Pbps (1015) Wireless ?
Fundamental dynamics: 3 + 1 rule
BS capacity
  Bandwidth: W
  Received power: Ps
  Min # of antennas: n
None of the three variables scales well!
RBS = n x W x log(1+SNR) = n x W x log(1+Ps /nWN0)
}
Notes: 112

## Slide 113: Gbps Wireless  Tbps (1012) Wireless  Pbps (1015) Wireless ?
Fundamental dynamics: 3 + 1 rule
BS capacity
  Bandwidth: W
  Received power: Ps
  Min # of antennas: n
None of the three variables scales well!
Ex 1: n = 16, W = 250 MHz, log(SNR) = 10  40 Gbps
RBS = n x W x log(1+SNR) = n x W x log(1+Ps /nWN0)
}
Notes: 113

## Slide 114: Gbps Wireless  Tbps (1012) Wireless  Pbps (1015) Wireless ?
Fundamental dynamics: 3 + 1 rule
BS capacity
  Bandwidth: W
  Received power: Ps
  Min # of antennas: n
None of the three variables scales well!
Ex 1: n = 16, W = 250 MHz, log(SNR) = 10  40 Gbps
Ex 2: n = 100, W = 7 GHz, log(SNR) = 15  10.5 Tbps
RBS = n x W x log(1+SNR) = n x W x log(1+Ps /nWN0)
}
Notes: 114

## Slide 115: Gbps Wireless  Tbps (1012) Wireless  Pbps (1015) Wireless ?
Fundamental dynamics: 3 + 1 rule
Network capacity
  # of BSs: K
Rnetwork = K x n x W x log(SNR)
}
Notes: 115

## Slide 116: Gbps Wireless  Tbps (1012) Wireless  Pbps (1015) Wireless ?
Fundamental dynamics: 3 + 1 rule
Network capacity
  # of BSs: K
Increasing BS capacity: Relatively difficult!
Increasing network capacity: Relatively easy!
Rnetwork = K x n x W x log(SNR)
}
Notes: 116

## Slide 117: Peak Rates
More bandwidth, more MIMO, more spectral efficiency (received power)
Notes: 117

## Slide 118: Peak Rates
More bandwidth, more MIMO, more spectral efficiency (received power)
Outdoors: More difficult to increase beyond tens of Gbps
Notes: 118

## Slide 119: Peak Rates
More bandwidth, more MIMO, more spectral efficiency (received power)
Outdoors: More difficult to increase beyond tens of Gbps
Indoors: Can increase towards Tbps
Ex 1: n = 16, W = 250 MHz, log(SNR) = 10  40 Gbps
Ex 2: n = 100, W = 7 GHz, log(SNR) = 15  10.5 Tbps
Enablers:
Higher frequencies, millimeter wave, THz, light  huge bandwidth
Short wavelength  massive MIMO
Pencil beams  interference rejection, high spectral efficiency
Notes: 119

## Slide 120: Peak Rates
More bandwidth, more MIMO, more spectral efficiency (received power)
Outdoors: More difficult to increase beyond tens of Gbps
Indoors: Can increase towards Tbps
Ex 1: n = 16, W = 250 MHz, log(SNR) = 10  40 Gbps
Ex 2: n = 100, W = 7 GHz, log(SNR) = 15  10.5 Tbps
Enablers:
Higher frequencies, millimeter wave, THz, light  huge bandwidth
Short wavelength  massive MIMO
Pencil beams  interference rejection, high spectral efficiency
More APs (small cells)
Network Capacity
Notes: 120

## Slide 121
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks
Part II: Technical Requirements

## Slide 122: Some Enabling Technologies in LTE-A Evolution
Carrier aggregation (licensed and unlicensed)
Advanced MIMO (multi-layer, adaptive beamforming)
D2D, terminal relaying (cellular-assisted multihop)
Advanced CoMP (cloud-RAN)
HetNet (heterogeneous networks)
SON+ (self-organizing, self-configuring, self-healing networks)
FeICIC (further enhanced intercell interference coordination)
Interference rejection (beamforming @ terminal)

## Slide 123: The Three Major Enabling 5G Technologies
Massive MIMO
Millimeter-wave
Small Cell

## Slide 124
Massive MIMO
Millimeter-wave
Small Cell
Not available anytime soon…
The Three Major Enabling 5G Technologies

## Slide 125
Massive MIMO
Millimeter-wave
Small Cell
Not available anytime soon…
The Three Major Enabling 5G Technologies
Cost…

## Slide 126: Latency
A. Sharifian, R. Schoenen, H. Yanikomeroglu, “Joint realtime and non-realtime flows packet scheduling and resource block allocation in wireless OFDMA networks”, IEEE Trans.Vehicular Tech, April 2016.
Notes: 126

## Slide 127: Latency
Is 1 ms round-trip delay possible?
Transmission at the speed of light:
(10-3 s) x (3x108 m/s) /2 = 150 km
Add buffering delay + queuing delay + scheduling delay + all types of protocol-induced delay
Notes: 127

## Slide 128: Latency
Is 1 ms round-trip delay possible?
Transmission at the speed of light:
(10-3 s) x (3x108 m/s) /2 = 150 km
Add buffering delay + queuing delay + scheduling delay + all types of protocol-induced delay
1 ms latency:
  D2D
  Edge-catching
  AI-based advanced prediction
Notes: 128

## Slide 129: Latency
Is 1 ms round-trip delay possible?
Transmission at the speed of light:
(10-3 s) x (3x108 m/s) /2 = 150 km
Add buffering delay + queuing delay + scheduling delay + all types of protocol-induced delay
1 ms latency:
  D2D
  Edge-catching
  AI-based advanced prediction
Latency is the new rate
Notes: 129

## Slide 130
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks
Part II: Technical Requirements

## Slide 131: Public Safety Networks
Terrestrial Trunked Radio (TETRA)
ETSI (European Telecommunications Standards Institute) standard
APCO-25
Association of Public-Safety Communications Officials – International (APCO)

## Slide 132: Commercial vs Public Safety & Tactical Communications
LTE Infrastructure for Command and Control Networks
Radisys While Paper, June 2013

## Slide 133: Recent Developments in USA
700 MHz spectrum for public safety
First Responder Network Authority (FirstNet) [22 Feb 2012]
  “FirstNet will provide a single interoperable platform for emergency and daily public safety communications”
  $100B
  LTE based
AT&T won the bid (2017)

## Slide 134: Public Safety in LTE-A

## Slide 135
From 4G to 5G
Near-term enabling technologies
Rate: Fundamental enablers
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks
Part II: Technical Requirements

## Slide 136: Radio Security: Threats and Vulnerabilities
New threats
Precision / targeted jamming
Solutions: Expensive

## Slide 137
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks
Part II: Technical Requirements

## Slide 138: WLAN: Renewed Momentum
802.11ad – 60 GHz, 6.8 Gbps
WiGig Alliance (subsumed by WiFi Alliance, Mar 2013)
802.11ac – 5 GHz, Gigabit WiFi (Feb 2014)
802.11af – TV whitespace (Jun 2014)
802.11ah – Sub 1 GHz, sensor networks (Jan 2016)
802.11ai – Fast initial link set-up (Feb 2015)
802.11p – DSRC (dedicated short-range communications)

## Slide 139: WLAN: Renewed Momentum
802.11ad – 60 GHz, 6.8 Gbps
WiGig Alliance (subsumed by WiFi Alliance, Mar 2013)
802.11ac – 5 GHz, Gigabit WiFi (Feb 2014)
802.11af – TV whitespace (Jun 2014)
802.11ah – Sub 1 GHz, sensor networks (Jan 2016)
802.11ai – Fast initial link set-up (Feb 2015)
802.11p – DSRC (dedicated short-range communications)
HEW: Highly Efficient WLAN
(study group: Mar 2013, task group: Jul 2014)
“dense network environments with large numbers of access points and stations”
802.11ax – 160 MHz @ 5 GHz, 10+ Gbps (2018-2019)

## Slide 140: Difference between Cellular and WLAN
WLAN: No coordination between APs, no interference management
  High peak rates
  Low edge rates
  Dense APs: Low rates
  Many users: Low rates
Test in Japan by NTT DoCoMo (2013)
Downlink speeds: LTE: 10 Mbps, WiFi: 1 Mbps

## Slide 141
From 4G to 5G
Rate: Fundamental enablers
Near-term enabling technologies
Public safety networks
Radio security: Threats and vulnerabilities
WLANs
Concluding remarks
Part II: Technical Requirements

## Slide 142: From Research to Deployment – A Long Journey
Standardization
Research
Conceptualization
Deployment

## Slide 143: From Research to Deployment – A Long Journey
Standardization
Research
Conceptualization
Deployment
4G
4G+, 5G
4G, 4G+, 5G,
5G+, 6G, …
5G+

## Slide 144: From Research to Deployment – A Long Journey
Standardization
Research
Conceptualization
Deployment
4G
4G+, 5G
5G+
From Invention/Envision to Standards:
4G, 4G+, 5G,
5G+, 6G, …

## Slide 145: From Research to Deployment – A Long Journey
Standardization
Research
Conceptualization
Deployment
4G
4G+, 5G
5G+
From Invention/Envision to Standards:
Invention (tangible subsystem, algorithm): 10 years
Ex: Polar codes: 2008  2018 (3GPP release 15)
4G, 4G+, 5G,
5G+, 6G, …

## Slide 146: From Research to Deployment – A Long Journey
Standardization
Research
Conceptualization
Deployment
4G
4G+, 5G
5G+
From Invention/Envision to Standards:
Invention (tangible subsystem, algorithm): 10 years
Ex: Polar codes: 2008  2018 (3GPP release 15)
Envision (system, architecture): Decades
Ex: Cooperative communications: 1971  5G/5G+ (?)
Ex: Totally autonomous vehicle: 1960s  2050 (?)
4G, 4G+, 5G,
5G+, 6G, …

## Slide 147: 5G  6G
Will 5G  6G roadmap be similar to 4G  5G roadmap?
  Near-term: Towards 2020 (5G standardization)
  Middle-term: early 2020s (5G evolution)
  Long-term: mid/late 2020s (6G discussions)
Notes: 147

## Slide 148: 5G  6G
Will 5G  6G roadmap be similar to 4G  5G roadmap?
  Near-term: Towards 2020 (5G standardization)
  Middle-term: early 2020s (5G evolution)
  Long-term: mid/late 2020s (6G discussions)
Many of the articulated scenarios, use cases, and technologies for 5G:
Will continue during 5G  6G era with a more mature market
Notes: 148

## Slide 149: 5G  6G
Will 5G  6G roadmap be similar to 4G  5G roadmap?
  Near-term: Towards 2020 (5G standardization)
  Middle-term: early 2020s (5G evolution)
  Long-term: mid/late 2020s (6G discussions)
Many of the articulated scenarios, use cases, and technologies for 5G:
Will continue during 5G  6G era with a more mature market
Ecosystem will likely be driven by new players
Notes: 149

## Slide 150
Looking forward to collaboration towards
6G wireless
http://www.sce.carleton.ca/faculty/yanikomeroglu/cv/publications.shtml
http://www.sce.carleton.ca/faculty/yanikomeroglu/cv/patents.shtml
http://www.sce.carleton.ca/faculty/yanikomeroglu/cv/theses.shtml
5G  6G will be very interesting

## Slide 151
Problem Statement and Solution Guidelines
HetHetNets: 5G+ Traffic Models
Ultra-Agile Networks for Wireless Ultra-Connectivity
  Spectrum
  Aerial BSs (Non-Terrestrial Networks
  User-in-the-Loop (UIL: Demand Shaping in Space & Time)
  Advanced PHY
    Optimized PHY with Massive Look-Up Tables
    Non-Coherent Communications
    Faster-Than-Nyquist Signaling
Concluding Remarks
Part III: Ultra-Agile Networks for Wireless Ultra-Connectivity (~250 slides)

## Slide 152
Challenge 1:
Extremely high traffic

## Slide 153: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic

## Slide 154: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic

## Slide 155: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic

## Slide 156: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic
Challenge 3: Nobody wants to pay for it!

## Slide 157: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic
Challenge 3: Nobody wants to pay for it!
Challenge 4: Novel services and applications

## Slide 158: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic
Challenge 3: Nobody wants to pay for it!
Challenge 4: Novel services and applications
new QoS requirements
more differentiation
rate
reliability
latency

## Slide 159: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic
Challenge 3: Nobody wants to pay for it!
Challenge 4: Novel services and applications
new QoS requirements
more differentiation
rate
reliability
latency
energy efficiency
cost
security

## Slide 160: Challenge 2: Extremely variable traffic
Challenge 1:
Extremely high traffic
Challenge 3: Nobody wants to pay for it!
Challenge 4: Novel services and applications
new QoS requirements
more differentiation
Challenge 5: Complex user

## Slide 161
Problem Statement and Solution Guidelines
HetHetNets: 5G+ Traffic Models
Ultra-Agile Networks for Wireless Ultra-Connectivity
  Spectrum
  Aerial BSs (Non-Terrestrial Networks
  User-in-the-Loop (UIL: Demand Shaping in Space & Time)
  Advanced PHY
    Optimized PHY with Massive Look-Up Tables
    Non-Coherent Communications
    Faster-Than-Nyquist Signaling
Concluding Remarks
Part III: Ultra-Agile Networks for Wireless Ultra-Connectivity (~250 slides)

## Slide 162
Vertical industries & novel use cases  Ultra demanding
Problem Formulation

## Slide 163
Vertical industries & novel use cases  Ultra demanding
Ultra-high speed
Ultra-high reliability
Ultra-low latency
Ultra-high # of connections
Ultra-high energy efficiency
Ultra-high security
Ultra availability
Ultra …
Problem Formulation

## Slide 164
Vertical industries & novel use cases  Ultra demanding
Ultra-high speed
Ultra-high reliability
Ultra-low latency
Ultra-high # of connections
Ultra-high energy efficiency
Ultra-high security
Ultra availability
Ultra …
Unpredictable and heavy-tail demand
Problem Formulation

## Slide 165
Vertical industries & novel use cases  Ultra demanding
Ultra-high speed
Ultra-high reliability
Ultra-low latency
Ultra-high # of connections
Ultra-high energy efficiency
Ultra-high security
Ultra availability
Ultra …
Unpredictable and heavy-tail demand
Cost efficient / Affordable
Problem Formulation

## Slide 166
Vertical industries & novel use cases  Ultra demanding
Ultra-high speed
Ultra-high reliability
Ultra-low latency
Ultra-high # of connections
Ultra-high energy efficiency
Ultra-high security
Ultra availability
Ultra …
Unpredictable and heavy-tail demand
Cost efficient / Affordable
Problem Formulation
Design the Network
?

## Slide 167
Vertical industries & novel use cases  Ultra demanding
Ultra-high speed
Ultra-high reliability
Ultra-low latency
Ultra-high # of connections
Ultra-high energy efficiency
Ultra-high security
Ultra availability
Ultra …
Unpredictable and heavy-tail demand
Cost efficient / Affordable
Problem Formulation
Ultra-Agile Network
for
Wireless-Ultra Connectivity

## Slide 168
Problem Statement and Solution Guidelines
HetHetNets: 5G+ Traffic Models
Ultra-Agile Networks for Wireless Ultra-Connectivity
  Spectrum
  Aerial BSs (Non-Terrestrial Networks
  User-in-the-Loop (UIL: Demand Shaping in Space & Time)
  Advanced PHY
    Optimized PHY with Massive Look-Up Tables
    Non-Coherent Communications
    Faster-Than-Nyquist Signaling
Concluding Remarks
Part III: Ultra-Agile Networks for Wireless Ultra-Connectivity (~250 slides)

## Slide 169
5G: Start of the ultra-connectivity era (W2.0)
Concluding Remarks

## Slide 170
5G: Start of the ultra-connectivity era (W2.0)
Brute-force approaches result in over-engineering  not feasible
An ultra-agile network is essential for efficient super-connectivity
Micromanage: Dynamic & adaptive from A-to-Z (opportunistically)
Concluding Remarks

## Slide 171
5G: Start of the ultra-connectivity era (W2.0)
Brute-force approaches result in over-engineering  not feasible
An ultra-agile network is essential for efficient super-connectivity
Micromanage: Dynamic & adaptive from A-to-Z (opportunistically)
Operator-user (client-server) distinction will get fuzzy
Novel architecture, novel enablers, novel business models, …
Concluding Remarks

## Slide 172
5G: Start of the ultra-connectivity era (W2.0)
Brute-force approaches result in over-engineering  not feasible
An ultra-agile network is essential for efficient super-connectivity
Micromanage: Dynamic & adaptive from A-to-Z (opportunistically)
Operator-user (client-server) distinction will get fuzzy
Novel architecture, novel enablers, novel business models, …
Need for a lot of exciting research and out-of-the-box thinking!
Concluding Remarks

## Slide 173
Looking forward to collaboration towards
6G wireless
http://www.sce.carleton.ca/faculty/yanikomeroglu/cv/publications.shtml
http://www.sce.carleton.ca/faculty/yanikomeroglu/cv/patents.shtml
http://www.sce.carleton.ca/faculty/yanikomeroglu/cv/theses.shtml
THANK YOU