## Slide 1: MPLS Technology fundamentals Sherif Toulan Technical Leader, Cisco Systems Canada
EDCS-1470619

## Slide 2: Sherif Toulan, Bio
Professional Engineers Ontario, P. Eng.# 90291410
M. Eng. Degree in Electrical Engineering from University of Toronto, 1991
Cisco Certified Internetwork Expert, CCIE# 4220, Routing & Switching
Project Management Professional, PMP# 511073
2000 – Present
Employed by Cisco Systems Canada as Network Design Engineer, working with key Service Providers (Bell Canada, at&t, France Telecom to deploy MPLS technologies)
1991-2000
Employed by Bell Canada as Network Consulting Engineer designing networks for Service Providers & Enterprise Customers (Banks, Insurance companies,…etc.)

## Slide 3: Agenda
MPLS Technology Basics
MPLS Traffic Engineering (TE)
MPLS Next Generation Technologies
Session Summary
“Topics”

## Slide 4: MPLS Technology Basics

## Slide 5: Agenda
Evolution of MPLS
MPLS forwarding basics
MPLS forwarding example
Summary

## Slide 6: Evolution of MPLS
“Technology Evolution and Main Growth Areas”
1997 1998 1999 2000 2001 2002 2003 2004 2005 2006 2007 2008 2009 2010 2011 2012 2013 2014
Bring MPLS to Market
Complete base MPLS portfolio
Optimize MPLS for video
Optimize MPLS for packet transport
Cisco ships MPLS
First L3VPNs Deployed
First MPLS TE Deployments
First L2VPN Deployments
Large Scale L3VPN
Deployments
Large Scale MPLS TE
Deployments
Large Scale L2VPN
Deployments
First MPLS Transport Profile Deployments
Evolved in 1996 & currently 99% of Service Providers have MPLS enabled in their networks
Key application initially were Layer-3 VPNs, followed by Traffic Engineering (TE), and Layer-2 VPNs
Notes: - A Request for Comments (RFC) is a publication of the Internet Engineering Task Force (IETF) and the Internet Society, the principal technical development and standards-setting bodies for the Internet.

## Slide 7: What Is Multi Protocol Label Switching (MPLS)?
Multi: | Multi-Protocol: The ability to carry any payload. Have:IPv4, IPv6, Ethernet, ATM, FR.
Protocol: | Could do IPX, AppleTalk, DECnet, etc.
Label: | Uses Labels to tell a node what to do with a packet; separates forwarding (hop by hop behavior) from routing (control plane)
Switching: | Routing: IPv4 or IPv6 lookup. Then forwarding is based on label Switching.
It’s all about labels …
Use the best of both worlds
  Layer-2 (ATM/FR): efficient & fast forwarding
  Layer-3 (IP) routing: flexible and scalable
MPLS forwarding plane
  Use of labels for forwarding Layer-2/3 data traffic
  Labeled packets are being switched instead of routed
    Leverage layer-2 forwarding efficiency
ATM = Asynchronous Transfer Mode
FR = Frame Relay
Notes: -Multiprotocol Label Switching (MPLS) is a mechanism in high-performance telecommunications networks that directs data from one network node to the next based on short path labels rather than long network addresses, avoiding complex lookups in a routing table. The labels identify virtual links (paths) between distant nodes rather than endpoints. MPLS can encapsulate packets of various network protocols. MPLS supports a range of access technologies, including ATM, Frame Relay, and DSL.
-Telecommunication networks:
http://en.wikipedia.org/wiki/Telecommunications_network
-Routing table: http://en.wikipedia.org/wiki/Routing_table
-ATM : http://en.wikipedia.org/wiki/Asynchronous_Transfer_Mode
-Frame Relay : http://en.wikipedia.org/wiki/Frame_Relay
-DSL : http://en.wikipedia.org/wiki/Digital_subscriber_line
-IPX protocol http://en.wikipedia.org/wiki/IPX/SPX
-DECnet protocol http://en.wikipedia.org/wiki/DECnet
-Asynchronous Transfer Mode “ATM”: http://en.wikipedia.org/wiki/Asynchronous_Transfer_Mode
-Frame Relay http://en.wikipedia.org/wiki/Frame_Relay

## Slide 8: Basic MPLS Forwarding Operations
“How MPLS Labels are Being Used to Establish label switched Path (LSP)?”
CE
CE
CE
CE
PE
PE
PE
Label Imposition (Push)
Label Swap
Label Disposition (PHP)
PE
Customer data
P
P
P
P
L1
L2
“FEC = Set of all packets that are going to be forwarded in exactly the same way”
“PHP= Penultimate hop popping”
MPLS Service Provider core
MPLS enabled Domain
1. PE (Provider Edge) router
  Label Edge router (LER)
  Imposes and removes MPLS labels
2. P (Provider) router
  Label switching router (LSR)
  Switches MPLS-labeled packets
3. CE (Customer Edge) router
  Connects customer network to MPLS network, no labels to be sent to CE nodes
Notes: - MPLS tutorial:
http://mplstutorial.com/mpls-basics
A FEC is a group/flow of packets that are forwarded along the same path and treating with the same with regards to forwarding treatment. All packets belonging to the same FEC have the same label. However not all the packets that have the same label belonging to the same FEC because their forwarding treatment could be different and they could belong to the different FEC. The router which decides which packets belong to which FEC is Ingress LSR.

## Slide 9: MPLS Label Switched Path (LSP) Setup
Label Distribution Protocol (LDP) signaling:
  Leverages existing routing protocols (OSPF, ISIS)
Exchange of MPLS labels
  Label bindings to IP addresses
  Downstream MPLS node advertises what label to use to send traffic to node
“LDP for LSP Signaling”
 | LDP
MPLS Forwarding path | - Label Switched Path (LSP)
MPLS Forwarding Calculation | - Based on IP routing database - Shortest-Path based
MPLS Packet Encapsulation | - Single or Multiple labels
MPLS Signaling | -By each node independently -Uses existing routing protocols/information
Notes: - MPLS networks must have LDP enabled
If Traffic Engineering is enabled then RSVP is used for signaling TE tunnels
LDP does not need to be enabled with MPLS TE

## Slide 10: IP Packet Forwarding Example
IP routing information exchanged between nodes
  Via IGP (e.g., OSPF, IS-IS)
Packets being forwarded based on destination IP address
  Lookup in routing table
“Basic IP Packet Forwarding” (No MPLS is enabled in the Service Provider network)
0
1
1
128.89.25.4
171.69.11.1
0
128.89.25.4
Data
128.89.25.4
Data
128.89.25.4
Data
…
128.89
171.69
Address
I/F
1
1
…
128.89
171.69
Address
I/F
0
1
…
128.89
171.69
Address
I/F
0
1
IP Forwarding Table
IP Forwarding Table
IP Forwarding Table
128.89.25.4
Data
1
OSPF = Open Shortest Path First
IS-IS = Intermediate System to Intermediate System
Notes: I/F = Interface port
IGP : Interior Gateway Protocol, i.e. routing protocol enabled to forward IP packets like OSPF (Open Shortest Path first), or ISIS Intermediate System to Intermediate System
Routers send packets toward their destination, by looking at the routing table & finding next hop to reach destination.
Routing protocols like OSPF (Open Shortest Path first), ISIS Intermediate System to Intermediate System (IS-IS) are used in core networks
Both IS-IS and OSPF are link state protocols, and both use the same Dijkstra algorithm for computing the best path through the network
Dijkstra algorithm http://en.wikipedia.org/wiki/Dijkstra%27s_algorithm

## Slide 11: MPLS Path (LSP) Setup with MPLS enabled
Enable IGP Routing (OSPF or ISIS) & MPLS LDP on all core links, i.e. PE-P & P-P links
Exchange of IP routes in core via:
  OSPF, IS-IS….,etc.
Establish IP reachability
Step 1: IP Routing (IGP) Convergence (MPLS enabled, i.e. LDP signaling is enabled)
128.89
171.69
In
Label
Address
Prefix
…
Out
I’face
128.89
1
171.69
1
…
Out
Label
In
Label
Address
Prefix
…
Out
I’face
128.89
0
171.69
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
You Can Reach 171.69 Thru Me
You Can Reach 128.89 and
171.69 Thru Me
Routing Updates (OSPF, ISIS, …)
You Can Reach 128.89 Thru Me
MPLS Forwarding Table
MPLS Forwarding Table
MPLS Forwarding Table
0
1
1
0
Notes: - IGP Routing protocol has to be enabled, i.e. OSPF or ISIS
- LDP has to be also enabled on all core links for MPLS before labels are advertised between nodes. If LDP is not enabled MPLS labels will not be built/advertised between core nodes
- Verify that reachability is achieved via ping or other means to ensure all IP subnets are advertised.

## Slide 12: MPLS Path (LSP) Setup with MPLS enabled
Local label mapping are sent to connected nodes
Receiving nodes update MPLS forwarding table
LDP label advertisement
Step 2: Assignment of MPLS Labels (MPLS enabled, i.e. LDP signaling is enabled)
1
128.89
Use Label 30 for 128.89
Use Label 20 for 128.89 and
Use Label 21 for 171.69
Label Distribution Protocol (LDP)
171.69
Use Label 36 for 171.69
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
1
1
…
Out
Label
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
0
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
20
21
…
-
-
…
30
36
…
20
21
…
-
…
30
…
MPLS Forwarding Table
MPLS Forwarding Table
MPLS Forwarding Table
)
0
1
1
0
Notes: 4- Labels are assigned to IP subnets & advertised via Label Distribution Protocol (LDP)

## Slide 13: MPLS Traffic Forwarding with MPLS enabled
Ingress PE node adds label to packet (push)
  Via MPLS forwarding table
Downstream node use label for forwarding decision (swap)
  Outgoing interface
  Out MPLS label
Egress PE removes label and forwards original packet (pop)
Step 3: Hop-by-hop Traffic Forwarding Using Labels (MPLS enabled, i.e. LDP signaling is enabled)
128.89.25.4
Data
128.89.25.4
Data
20
128.89.25.4
Data
30
Forwarding based on Label
128.89.25.4
Data
128.89
171.69
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
1
1
…
Out
Label
In
Label
Address
Prefix
128.89
171.69
…
Out
I’face
0
1
…
Out
Label
In
Label
Address
Prefix
128.89
…
Out
I’face
0
…
Out
Label
20
21
…
-
-
…
30
36
…
20
21
…
-
…
30
…
MPLS Forwarding Table
MPLS Forwarding Table
MPLS Forwarding Table
0
1
1
0
Notes: - PE nodes remove labels before sending to CE devices since they do not understand MPLS, only IP

## Slide 14: MPLS Traffic Forwarding with Label Distribution Protocol (LDP) “Summary”
MPLS increases the speed & performance in Service Provider Network by doing forwarding based on labels
The MPLS enabled routers (LSRs, LERs) use Label Distribution Protocol (LDP) to assign & distributes labels, LDP is the signaling protocol used by MPLS
The MPLS enabled routers advertise their labels to other MPLS enabled routers, the labels advertise reachability across MPLS network
No labels are advertised to Customers

## Slide 15: MPLS Traffic Engineering

## Slide 16: Agenda
MPLS Traffic Engineering (TE) motivation
MPLS TE Path Selection - Constraint-Based Shortest Path First (CSPF)
MPLS TE signaling – LSP Setup – Resource Reservation Protocol (RSVP)
Summary

## Slide 17: Link Utilization problem with IGP (OSPF or ISIS)
PE1
P1
P4
P2
P3
P5
PE4
PE3
PE2
IP (Mostly) Uses Destination-Based Least-Cost Routing
Flows from PE1, PE2 Merge at P1 and Become Indistinguishable
Upper path is over-utilized
“Lower Path will be Under-Utilized”
Cost=10
Cost=10
Cost= 10
Cost= 10
IGP = Interior Gateway Protocol (OSPF or IS-IS)
MPLS core
40Mbps
40Mbps
80Mbps
80Mbps
Cost=10
Notes: http://en.wikipedia.org/wiki/Dijkstra's_algorithm
SPF algorithm is explained in the above link

## Slide 18: What MPLS-TE Technology solves?
Node | Next-Hop
PE3 | Tunnel 1
PE4 | Tunnel 2
MPLS TE solves link utilization problem, i.e. no oversubscription
P1 is the HEADEND & sees all the links
P1 computes paths on properties other than just least cost
Tunnel 1, Tunnel 2 are manually configured & path is explicitly enabled from P1 to P3
Tunnel 1 will take path P1-P2-P3
Tunnel 2 will take different path P1-P4-P5-P3
40Mb
40Mb
P1
P2
P4
P3
P5
PE3
PE4
Tunnel 1
Tunnel 1
Tunnel 2
Tunnel 2
Tunnel 2
MPLS core
40Mb
40Mb
40Mb
40Mb
Notes: -Traffic engineering refers to the process of selecting the paths that traffic will transit through the network. Traffic engineering can be used to accomplish a number of goals. For example, a network organization could traffic engineer their network to ensure that none of the links or routers in the network are over or under utilized. Alternatively, a network organization could use traffic engineering to control the path taken by voice packets in order to ensure appropriate levels of delay, jitter, and packet loss.
MPLS supports traffic engineering thus allowing network organizations to associate a Label-Switched Path (LSP) with whatever physical path they choose. MPLS also supports constraint-based routing, which ensures that an LSP can meet specific performance requirements. In addition, tools that work on a per-LSP basis allow network organizations to identify usage levels and plan accordingly.

## Slide 19: MPLS Traffic Engineering (MPLS TE) “Resource Reservation Protocol - Traffic Engineering (RSVP-TE) Building Blocks”
Step 2:
CSPF does Path Calculation on Headend only – uses IGP advertisements to compute “constrained” paths, CSPF takes into account: bandwidth, Link attributes, Admin weight
Step 3:
Path Setup-
RSVP used to provide Link Admission Control, failure notification, etc.
Step 1:
Information Distribution - IGP (OSPF or IS-IS) extensions used to flood IGP topology & link attributes information between routers, i.e. Traffic Engineering Database (TED)
Headend
Midpoint
Tail
RSVP-TE Tunnel is UNI-DIRECTIONAL!
RSVP state is maintained across all Nodes
10
10
10
10
10
Step 4:
Forwarding traffic:
Static route, auto route announce,….etc.
Data mapped to TE Tunnel 1
Voice mapped to TE Tunnel 2
IS-IS Single level
10
10
IS-IS = Intermediate System to Intermediate System
TE Tunnel 1
TE Tunnel 2

## Slide 20: Constraint-Based Shortest Path First (CSPF) for path computation
MPLS
TE Topology database
From IGP
extended database
5
3
10
15
10
10
8
10
R1
Tunnel
Headend
R8
Tailend
Link with insufficient bandwidth
Link with sufficient bandwidth
n
n
Find shortest path to R8 with 8Mbps
IGP database extensions advertise bandwidth & other link attributes, IGP database extensions makes the Traffic Engineering Database (TED)
CSPF uses Traffic Engineering Database (TED) to find best path for TE tunnel that meets the user constraints & path requested
Tunnel can be signaled via Resource Reservation Protocol (RSVP) once a legitimate path is found
Notes: Constrained Shortest Path First (CSPF) is an extension of shortest path algorithms. The path computed using CSPF is a shortest path fulfilling a set of constraints. It simply means that it runs shortest path algorithm after pruning those links that violate a given set of constraints. A constraint could be minimum bandwidth required per link (also known as bandwidth guaranteed constraint), end-to-end delay, maximum number of links traversed, include/exclude nodes. CSPF is widely used in MPLS Traffic Engineering. The routing using CSPF is known as Constraint Based Routing (CBR).
The path computed using CSPF could be exactly same as that of computed from OSPF and IS-IS, or it could be completely different depending on the set of constraints to be met.

## Slide 21: How to map Customer Traffic into a TE tunnel?
Multiple traffic selection options:
  Static routes
  Policy Based Routing (specific match criteria)
Traffic enters tunnel at head end
MPLS core
Tunnel Head end
TE LSP
Customer Traffic
TE LSP = Traffic Engineering label switched path
Notes: In computer networking, policy-based routing (PBR) is a technique used to make routing decisions based on policies set by the network administrator.
When a router receives a packet it normally decides where to forward it based on the destination address in the packet, which is then used to look up an entry in a routing table. However, in some cases, there may be a need to forward the packet based on other criteria. For example, a network administrator might want to forward a packet based on the source address, not the destination address. This should not be confused with source routing.
Policy-based routing may also be based on the size of the packet, the protocol of the payload, or other information available in a packet header or payload. This permits routing of packets originating from different sources to different networks even when the destinations are the same and can be useful when interconnecting several private networks.
Link:
http://en.wikipedia.org/wiki/Policy-based_routing

## Slide 22: MPLS Traffic Engineering “Summary”
Traffic Engineering (TE) tunnels are used to manipulate the traffic across the Service provider core networks & override default IGP behavior, i.e. forward based on least cost
Traffic Engineering (TE) tunnels provide efficient utilization of links based on available bandwidth & defined user constraints.
Traffic Engineering (TE) tunnels use CSPF to establish the path & RSVP for signaling the TE tunnels
CSPF used the Traffic Engineering Database (TED) that is built from IGP database TE extensions
Customer traffic can be mapped to TE tunnels either by static route or Policy based routing to follow a specific path across the core network & as defined in Service Level Agreements between Service Provider & Customer.
RSVP = Resource Reservation Protocol
IGP = Interior Gateway protocol
TE = Traffic Engineering

## Slide 23: MPLS Next Generation Technologies

## Slide 24: Agenda
Motivation for Next Generation MPLS technologies
Application Engineered routing
Summary

## Slide 25: The Full MPLS integrated Network: “MPLS VPN services,Traffic Engineering technologies”
CE
PE
PE
CE
CE
CE
Layer 2 Circuits available – Ethernet, ATM, Frame Relay, PPP, HDLC
MPLS Backbone
LDP & RSVP both enabled
Traffic Engineering
Internet
Gateway
Internet
Layer 2 Circuits available – Ethernet, ATM, Frame Relay, PPP, HDLC
Layer 2 Circuits available – Ethernet, ATM, Frame Relay, PPP, HDLC
Layer 2 Circuits available – Ethernet, ATM, Frame Relay, PPP, HDLC
Notes: Virtual Leased Line,
SP deploy once and deliver many services
Enterprise – a set of equipment and many services

## Slide 26: Segment Routing Value Proposition “Simplify the MPLS transport”
PE
PE
CE
Internet
Gateway
Internet
CE
CE
CE
MPLS VPN services, TE are enabled
CE
CE
CE
CE
MPLS VPN services, TE are enabled
Cont.
Segment Routing replaces Label Distribution Protocol (LDP) for MPLS control plane:
  IGP (IS-IS or OSPF) + LDP  IGP (IS-IS or OSPF) with Segment Routing extension = Better Scale
Segment Routing replaces Resource Reservation Protocol (RSVP) to build Engineered Label Switched paths (LSP):
  RSVP Traffic engineering (RSVP-TE)  Segment Routing Traffic engineering (SR-TE) = Ease of deployment & troubleshooting
Segment Routing
Notes: Use Animation to bring bullets one by one & not all at once
Focus on MPLS services still use Segment Routing as MPLS transport = Simplify MPLS transport
Bring in the diagram with animation at last

## Slide 27: Segment Routing packet forwarding
Source Routing along with the explicit path, stack of prefix and adjacency segments
Any explicit path Engineered SR-TE can be expressed:
  e.g. ACOZ – Loose source routing
  or ABCOPZ– Strict source routing
Per-flow state only at head-end
  not at midpoints
SR-TE = Segment Routing traffic Engineering
A
B
C
M
N
O
Z
D
P
Pop 9003
Packet to Z
16065
9003
Packet to Z
16065
Packet to Z
Packet to Z
16065
Packet to Z
16065
9003
16072
Packet to Z
16065
9003
16072
16072
16072
16065
16065

## Slide 28: Segment Routing for Application Engineered Routing “Centralized SDN Controller”
  Centralized Optimization for the Path via an SDN controller (Path Computation element “PCE”):
              Tight Integration of Applications with Segment Routing & SDN Controller
              SDN Controller engineers the Segment Routing path to meet the Service Level Agreement (SLA)
Download the path to meet Application
SLA to node Z {66, 9001, 65}
66
65
9001
SDN Controller engineers & downloads the Path that meets Application SLA via Path Computation Element Protocol (PCEP)
Congested
Collect network
status information
Need 2Gbps from Toronto to Vancouver with SLA
SDN= Software Defined Networking
SLA = Service Level Agreement
Toronto
Winnipeg
Edmonton
Whitecourt
Thunder Bay
Montreal
Calgary
Kelowna
Vancouver
SDN
Controller
“PCE”
Notes: Focus on how Segment routing is now closer to applications

## Slide 29: MPLS session
Key Takeaways
MPLS networks consist of PE routers at ingress/egress and P routers in the core
MPLS forwarding operations is based on MPLS labels, hence it speeds up the performance
Label Distribution Protocol (LDP) is used for MPLS signaling & assigning MPLS labels to IP addresses (prefixes)
Routing protocols (OSPF or IS-IS ) enabled in the core network has to be working properly for proper MPLS forwarding operation
Traffic Engineering manipulates that path of traffic to better utilize bandwidth & meet Service Level agreements between Service Provider & Customer
Resource Reservation Protocol (RSVP) is used for Traffic Engineering signaling & setup
MPLS & its associated technologies are widely deployed across both Service Provider & Enterprise networks
OSPF = Open Shortest Path First
IS-IS = Intermediate System to Intermediate System

## Slide 31: Acronyms
Acronym | Description
MPLS | Multi Protocol label switching
TE | Traffic Engineering
VPN | Virtual Private Network
ATM | Asynchronous transfer mode
FR | Frame relay
IP | Internet protocol
FEC | Forwarding equivalence class
LDP | Label distribution protocol
LSP | Label switched path
TOS | Type of service
RSVP | Resource reservation protocol
OAM | Operation, administration, maintenance
BGP | Border gateway protocol
TTL | Time to live
QoS | Quality of service
IGP | Interior gateway protocol
OSPF | Open shortest path first
MAC | Media Access Control
LAC | Link Admission Control
Acronym | Description
IS-IS | Intermediate system to intermediate system
LSR | Label switch router
LER | Label edge router
CSPF | Constraint-based shortest path first
PBR | Policy based routing
PW | Pseudo wire
VPLS | Virtual private LAN service
VPWS | Virtual private wire service
EVPN | Ethernet Virtual Private Network
PBB-EVPN | Provider backbone bridging Ethernet Virtual Private Network
PSN | Packet Switched network
VLAN | Virtual local area network
HDLC | High-level data link control
PPP | Point-to-point protocol
IGP | Interior gateway protocol
RIPv2 | Routing information protocol version 2
EIGRP | Enhanced Interior Gateway Routing Protocol
OAM | Operation, Administration & Maintenance