## Slide 1: Modeling with Automata
Component-driven modeling. Finite State Machines. Petri Nets.

## Slide 2: System dynamics Paradigms
System Dynamics : A sequence of State transitions
Model : A set of rules for a State transition
Review
Differential
Equations
(physical
system)
Difference
Equations
(sampled
system)
Timed Automata,
DEVS
Digital
System
(Digital
Voice,
FSM)
CVDS
DTDS
DDS
DEDS
System
S
X
Y

## Slide 3: System dynamics Paradigms
System Dynamics : A sequence of State transitions
Model : A set of rules for a State transition
System
S
X
Y

## Slide 4: Dynamic Systems representations
Simulator:
Events
Processor
DEVS: discrete event
System
DEVS model
time to next event,
state at next event ...
DTSS: difference equation
Simulator:
Recursive
Algorithm
System
DTSS model:
q(t+1) = a*q(t)+ b*x(t)
DESS: differential equation
System
Simulator:
Numerical
Integrator
DESS model:
dq/dt = a*q +bx
System Specifications:

## Slide 5: Systems theoretical modelling
Behavioral models: ‘Black boxes’.
  Define input/output behavior.
  Representation of observable and non-observable variables .
Structural models: ‘White boxes’.
  Represent system internal structure.
  Decomposition and coupling.
  Refers to elements in a model as opposed to the behavior it generates.
Different formalisms derived from these ideas.
Notes: En esta clase nos vamos a concentrar en formalismos tipo White Box, en particular FSM

## Slide 6: Component definition
Component: viewed as a model with inputs and outputs.
It has internal structure which dictates how inputs/states are transformed to outputs.
Components are coupled together to create models, which themselves can be components in larger models.
states
functions
INTERNAL STRUCTURE
inputs
outputs
Notes: Vamos a seguir una estrategia de modelado por componentes

## Slide 7: Component-based system dynamics
To capture system’s dynamics, we need to represent states and how they change over time, autonomously and/or in response to external events:
  Inputs
  States
  Outputs
  Time it takes for an activity to be completed
  Internal Dynamics

## Slide 8: Finite State Machines
FSM = < S, X, Y, ,  >
  X : input set
  Y : output set
  S : state set
  ,  : functions with the following constraints
    X, Y, S : finite sets
     : X * S  S
     : S  Y : Moore machine
     : X * S  Y : Mealy machine
Untimed discrete event system
Timed versions of FSMs associate time with states or transitions.
S


x
y

## Slide 9: Finite State Machines
FSM = < S, X, Y, ,  >
  X : input set
  Y : output set
  S : state set
  ,  : functions with the following constraints
    X, Y, S : finite sets
     : X * S  S
S


x
y
Notes: Every FSM is supposed to have an initial state, a next-state function that defines how to obtain
the next state in the system, and an output function that uses current state and inputs to generate outputs.
According to the relationship between the input sets and output functions, two kinds of FSMs
can be defined: Moore machines, in which outputs are independent from the inputs, and Mealy
machines, in which, besides the current state variables, the current inputs are analyzed to decide the current output value.

## Slide 10: Finite State Machines
Moore machines:
  non-reactive
(response delayed by 1 cycle)
  easy to compose
Always well-defined.
FSM = < S, X, Y, ,  >
  X : input set
  Y : output set
  S : state set
  ,  : functions with the following constraints
    X, Y, S : finite sets
     : X * S  S
     : S  Y : Moore machine
S


x
y
Notes: Every FSM is supposed to have an initial state, a next-state function that defines how to obtain
the next state in the system, and an output function that uses current state and inputs to generate outputs.
According to the relationship between the input sets and output functions, two kinds of FSMs
can be defined: Moore machines, in which outputs are independent from the inputs, and Mealy
machines, in which, besides the current state variables, the current inputs are analyzed to decide the current output value.

## Slide 11: Finite State Machines
Moore machines:
  non-reactive
(response delayed by 1 cycle)
  easy to compose
Always well-defined.
Mealy machines:
  reactive
(0 response time)
  hard to compose
Problems with combinational cycles.
FSM = < S, X, Y, ,  >
  X : input set
  Y : output set
  S : state set
  ,  : functions with the following constraints
    X, Y, S : finite sets
     : X * S  S
     : S  Y : Moore machine
     : X * S  Y : Mealy machine
S


x
y
Notes: Every FSM is supposed to have an initial state, a next-state function that defines how to obtain
the next state in the system, and an output function that uses current state and inputs to generate outputs.
According to the relationship between the input sets and output functions, two kinds of FSMs
can be defined: Moore machines, in which outputs are independent from the inputs, and Mealy
machines, in which, besides the current state variables, the current inputs are analyzed to decide the current output value.

## Slide 12: Example: FSM modeling
Queue
in
Server
out
Banking system: Queue+Server
(1) Conceptual Model
components
descriptive variables (state variables)
dependency: interaction between components
(i) Descriptive variables
  Queue length: [0 ... N]
  “queue.length = n”: n customers in the waiting line
  Server’s status: [Busy, Free]
(ii) Interaction with outside world
  When a customer arrives:
    System puts it in the queue
    Serve customer (in some specified time)
    Send customer out

## Slide 13: FSM formal definition
0
1
2
N
in
in
in
in
out
out
out
(2) Formal model specification: M = <X, Y, S, ,  >
From informal description, the following should be specified
  (i) Identify X, Y, S
  (ii) State transition function
  (iii) Output function
(3) Case I : state : Queue Length
  M = <X, Y, S, ,  >
  X = {in}
  Y = {out}
  S = {queue.length in [0, N]}
   : X * S  S
  (in, n) = n+1 for all n<N (Obs: there is no out in transition function)
   : S  Y
  (n0) = out
Problem : queue.length never decreases
 solution : introduce a feedback to notify that a customer is leaving
…
Queue
in
out
Notes: La idea: modelar es util; no hay q simular p/encontrar problemas.
Este es un ejemplo c/problemas. Queremos hacer la FSM de la slide 11.
El modelo de la 12 es la cola separada del resto; problema: crece pero no decrece nunca. Porque? Xq no se entera q la gente salio. Simplemente mirando la notacion grafica te das cuenta q hay un error. Es importante modelar. La gente codifica directamente y estas cosas NO SE VEN. En cambio, aca, abris los ojos y el error salta, antes de empezar ningun ‘simulador’.

## Slide 14: Modified formal definition: queue
0
1
2
N
in
in
in
in
out
out
out
done
done
done
done
‘done’ is introduced by feedback
<Modified>
M = <X, Y, S, ,  >
  X = {in, done}
  Y = {out}
  done = out
  S = {queue.length in [0,N]}
   : X * S  S
  (in, n) = n+1 for all 0  n <N
  (done, n) = n-1 for all 0 < n N
   : S  Y
  (n0) = out
Queue
in
out
Feedback
done
…
Notes: La FSM de la cola arreglada, con un feedback loop para solucionar el problema. Out se conecta c/done; done avisa q alguien se fue; hace reducir la cantidad de gente en la cola. C/out engancha c/el feedback, va a done, done decrementa en 1.

## Slide 15: Formal definition: server
(3) Case II : state : Server Status
  M = <X, Y, S, ,  >
  X = {in, done}
  Y = {out} done = out
  S = server.status in [B, F]
   : X * S  S
  (in, B) = B
  (in, F) = B
  (done, B) = B if queue.length > 1
F if queue.length <= 1
  (done, F) = N/A
   : S  Y
  (S=B) = out
B
F
in
done (|q|1)
in
done (|q|>1)
out
in
Server
out
Feedback
done
in
done
done
out
out
in
server
server
Notes: OJO ! Server se define usando variables que pertenecen a queue. Por eso están adentro de la misma “caja”. Esto muestra que se “comunican” las FSM.
Observar: NO HAY envío de información “desde” queue a server, como vamos a estar viendo en DEVS.
El servidor. Es la FSM de arriba y el código q esta a la izquierda.
Una vez q tenemos el servidor y la cola, hay q acoplarlos. Se acopla como en el acoplamiento de abajo. Los 2 in de arriba: uno va a queue. En queue, encola una persona. Otro va a in. si miras la FSM q esta en esa slide, in solo hace pasar al server de Free a Busy. Tiene q saber q vino alguien p/decir: “ahora estoy ocupado atendiendo al primero”.
Cuando alguien se va del server, ese out se conecta c/done, q lo pone en free si queda una sola persona.
Y el mismo out se usa para liberar una persona de la queue.
Basicamente, hay 2 FSM, separadas, y los in/out hacen, en c/u de ellas, y x separado, lo q se supone q tienen q hacer. Por separado.

## Slide 16: Communicating FSM (CFSM)
Collections of FSMs connected together
  Logical analysis of concurrent system (Safety property, Liveness property)
  Modeling : a set of FSMs
  Execution : global state transition by local state transition rules
Communicating method
  Asynchronous
    Coupling FSMs via a queue
  Synchronous
    Special case of Asynchronous with length(queue) = 1
    Coupling FSMs directly through input/output
Notes: properties: true for every possible execution
safety: nothing bad happens
liveness: something good eventually happens
Ver con Gabriel: ¿Cual es el razonamiento para esto? (lo saqué):
  Modeling a CFSM
    one state transition system in a whole
    no distinction of input, output, hidden events
Ver con Gabriel: Eliminé Slide:“CFSM rules” (buscarla en la clase de 2009 y 2010) Quiero tener bien la explicación: Gabriel ?
Dice esto:
  System rules
    synchronous
      selection of a pair of common events
      resolution of conflict pairs of common event
    asynchronous
      defining input/output to be conditional on the state of the queues
      input queue is empty  No input event is available  No state transition
      output queue is full  No output event is produced
  Execution rules
    Transition only one FSM
    At most two FSMs perform state transition in one time stamp
    Two step algorithm
      (1) select a pair of events to be applied
      (2) execute transition ; go to (1)

## Slide 17: CFSM State Set: queue + server
in
in
done
done
done
done
done
done
Server.status
B
F
queue.length
1
2
3
0
N
N-1
N-2
N-3
out
out
out
out
out
out
out
: undefined state
< Case I + Case II >
 : X * S  S
S = {(queue.length, server.status) | queue.length is in [0 ... N] and server.status  [B, F]}
in
in
in
in
in

## Slide 18: Formal definition of CFSM
Formal specification of CFSM
  CFSM = < E , Q , q0 , T , {FSM} >
    E : Events set
    Q : States set
    q0 : Initial state
    T : Transition relations
    FSM : ith FSM
    With the following constraints:
Notes: Notar que los included contemplan que no sea la totalidad de las posibilidades, ya que puede haber prohibiciones sobre ciertas “transiciones” y “estados combinados”.

## Slide 19: Example: Synchronous Machine of ping-pong players
A_D
A_A
Ball_B
Ball_A
/Ball_A
Ball_B
player_A
player_A = <XA, YA, SA, A, A >
player_B = <XB, YB, SB, B, B>
XA = {Ball_B}
YA = {Ball_A}
SA = {A_A, A_D}
A , A : exercise
XB = {Ball_A}
YB = {Ball_B}
SB = {B_A, B_D}
B, B : exercise
B_D
B_A
Ball_A
Ball_B
/Ball_B
Ball_A
player_B

## Slide 20: CFSM for the ping-pong example
D
A
/Ball_A
Ball_B
player_A
D
A
/Ball_B
Ball_A
player_B
Ball_A
Ball_A
Ball_B
Ball_B
Problem : player_A output: Ball_A. Transition ?
A_A, B_D
A_D, B_A
Ball_A
Ball_B
CFSM
A_A
A_D
/Ball_A
Notes: Problema: En el jugador A, cuando viene Ball_B está claro que pasa. Pero que es lo que hace que cuando estoy en A_A me vaya a A_D ?
Tengo que inventar un “evento interno” que no debería depender de ningún fenómeno externo …

## Slide 21: CFSM for the ping-pong example
D
A
/Ball_A
Ball_B
player_A
D
A
/Ball_B
Ball_A
player_B
Ball_A
Ball_A
Ball_B
Ball_B
A_A, B_D
A_D, B_A
Ball_A
Ball_B
CFSM
Player_A  : X  S  S
XA = {Ball_B}  {} : internal event
A_A
A_D
Ball_A
A_A
A_D

Ball_A
feedback
A_A
A_D
/Ball_B
Ball_A
Ball_B


feedback
Notes: Problema: En el jugador A, cuando viene Ball_B está claro que pasa. Pero que es lo que hace que cuando estoy en A_A me vaya a A_D ?
Tengo que inventar un “evento interno” que no debería depender de ningún fenómeno externo …

## Slide 22: CFSM for the ping-pong example (cont)
A_A, B_D
A_D, B_A
Ball_A
Ball_B
CFSM = <E, Q, q0, T, {player_A, player_B}>
  E = XiYiXjYj = {Ball_A, Ball_B}
  q0 = (A_A, B_D)
  Q SA  SB ({(A_A, B_D), (A_D, B_A)} = Q}