## Slide 1
SYSC 5608
Wireless Communication Systems Engineering
Introduction to the Course
Halim Yanikomeroglu, PhD, PEng
Professor
Department of Systems & Computer Engineering
Carleton University
Ottawa, Canada

## Slide 2: What is Wireless Communications? 1/2
Electromagnetic waves
  Mainly, radio waves (3 KHz to 300 GHz or 3 THz) [http://en.wikipedia.org/wiki/Radio_spectrum]

## Slide 3: ITU (International Telecommunications Union) Radio Bands
ITU Radio Bands | Frequency Range (f) |  | Wavelength Range (l) |  | 
HF | 3 MHz | 30 MHz | 100 m | 10 m | 
VHF | 30 MHz | 300 MHz | 10 m | 1 m | 
UHF | 300 MHz | 3 GHz | 1 m | 10 cm | 1G – 4G
SHF | 3 GHz | 30 GHz | 10 cm | 1 cm | 
EHF | 30 GHz | 300 GHz | 1 cm | 1 mm | mmWave
THF | 300 GHz | 3 THz | 1 mm | 0.1 mm | THz comm
Carrier frequency vs bandwidth
Wavelength: l = c/f, where c = 3x108 m/s and f is the carrier frequency (Hz)
Bandwidth: Difference between upper and lower frequencies around the carrier

## Slide 4: What is Wireless Communications? 1/2
Electromagnetic waves; travel through vacuum
  Mainly, radio waves (3 KHz to 300 GHz or 3 THz) [http://en.wikipedia.org/wiki/Radio_spectrum]
  Some use “wireless communications” and “radio communications” interchangeably; but,
    a) “radio” generally highlights only the propagation aspect,
    b) not all wireless is radio.
  “Wireless” is much broader than “radio”.
  Likewise, some use “mobile communications” and “radio communications” interchangeably. But, “wireless” has many other aspects in addition to being “mobile”.
  More recently: terahertz comms, free-space optical (FSO) comms
Mechanical waves; requires a material medium (outside our scope)
Ex: Sound waves (20 Hz – 20 KHz); not electromagnetic

## Slide 5: What is Wireless Communications? 2/2
A large number of phenomena, components, and sub-systems
  Ex: Fading phenomenon
Interacting in highly complex manners
  Ex: 5G wireless networks
Wireless systems may be very complex
  Ex: 4G LTE and LTE-Advanced standards: thousands of pages
  One of the most advanced and sophisticated engineering systems ever
Wireless is a multi-disciplinary area
  Electrical engineering, computer engineering, computer science, applied mathematics, …

## Slide 6: SYSC 5608 Scope
Wireless: different from wired communications
  Limited power and bandwidth  limited capacity
  Channel  inferior quality
  Broadcast nature  Users are tangled
   Network problem (not a link problem)
Layers in the protocol stack
  L0: Propagation ***
  L1: Physical layer (PHY) **
  L2: Medium access layer (MAC) ***
  L3: Networking layer (NET) *
Note that L0 and L2 are the distinguishing layers

## Slide 7: SYSC 5608 Scope
Wireless: very broad  many courses
SYSC 5608
  systems course
  touches upon all layers and many applications
  less focused
ELG 5133 (SYSC 5606) Introduction to Mobile Communications
  more focused, mainly PHY
ELG 7177C Topics in Comm. 1: Wireless Ad Hoc Networking
  One important application
ELG 5132 Smart Antennas
  One important PHY technology
SYSC 5403 Network Access Techniques
SYSC 5700 Spread Spectrum Systems
  One important multiple access scheme
SYSC xxxx Topics in Comm.: Cross-Layer Design

## Slide 8: Protocol Layers
Understanding propagation and channel
  propagation modeling
  received power
  received power’s large-scale and small-scale variations and statistics
L1 PHY: Developing techniques to improve the performance for a given channel (SNR and it’s statistics)
[Why SNR statistics is important?]
  channel coding
  diversity
  equalization, …
L2 MAC: Sharing the medium and radio resources
  radio resource management (RRM)
L3 NET: Sharing the radio access network (RAN)
  routing, …

## Slide 9: Protocol Layers
L2 + L3: for each terminal, determine
  at what time to transmit (time scheduling)
  at what frequency to transmit (frequency scheduling)
  at what power to transmit (power scheduling)
  at which PHY mode to operate (eg., adaptive modulation and coding)
  to which RAN element to connect (macro-BS, pico-BS, WiFi-AP, relay, …)
based on (objective function and constraints)
  maximizing user rate (throughput)
  maximizing aggregate network throughput
  minimizing latency
  attaining fairness (ubiquitous coverage)
  maximizing energy efficiency
  …
L2 + L3: assignment problems  optimization

## Slide 10: Why Should You Know Wireless?
ICT (information and communication technologies): trillion-dollar industry
Wireless: one of the most essential components of ICT
Its relevance will increase substantially in the foreseeable future
 vertical industries
Work opportunities
  Vendors (Ericsson, Huawei, Nokia, …)
  Operators (Bell Mobility, Rogers, Telus, …)
  Chipmakers (Intel, Qualcomm, MediaTek, Broadcom, …)
  Start-ups
  Other ICT/computing industries (Google, Amazon, Facebook, …)
  Verticals (health, automotive, agriculture, defence, entertainment, …)
  Government
  Graduate studies
  …

## Slide 11: Remarks
I will use the slides as well as the board – You are responsible from both
Beginning of each day: A brief discussion about
  Previous lectures
  Emerging wireless technologies
  Other technical concepts
  Career related issues, graduate studies
  Popular topics
I will provide light reading materials
Subscribe to wireless news portals, such as
FierceWireless @ http://www.fiercewireless.com

## Slide 12: Remarks
From me
I have been preparing for this course for 30 years…
Not an over-the-weekend preparation
An area that I know well; I have expertise in many sub-areas
I am excited and highly motivated

## Slide 13: Remarks
From me
I have been preparing for this course for 30 years…
Not an over-the-weekend preparation
An area that I know well; I have expertise in many sub-areas
I am excited and highly motivated
From you
Make sure that you have sufficient background in digital comm
Attend lectures
Be motivated, show interest, take it serious, work hard
 Most important factors in success!
Utilize the opportunity

## Slide 14: Remarks
From me
I have been preparing for this course for 30 years…
Not an over-the-weekend preparation
An area that I know well; I have expertise in many sub-areas
I am excited and highly motivated
From you
Make sure that you have sufficient background in digital comm
Attend lectures
Be motivated, show interest, take it serious, work hard
 Most important factors in success!
Utilize the opportunity
I want to give good grades; please help me!

## Slide 15: Course Approach 1/5
The course includes both analysis and synthesis parts.
This course has the systems view
(not a physical layer course, not a networking course;
rather, a systems course)
The emphasis is on the multiple access and related issues; the course also covers certain aspects of radio propagation, physical layer, medium access control (MAC) layer and networking layer.
The course covers a broad range of topics:
  Fundamental dynamics
  Components in isolation
  Integrated systems
Therefore, this is an introductory graduate course

## Slide 16: Course Approach 2/5
One way of partitioning wireless:
  Cloud
  Pipe
  Devices
which are all tangled.
This course is mainly on the pipe (connectivity), but we will cover certain aspects of wireless devices (for instance, signal processing and algorithmic aspects) as well as the cloud (super network).

## Slide 17: Course Approach 3/5
Two fundamental questions in wireless:
This course addresses the following fundamental question:
“How can we increase the performance of wireless networks by efficient utilization of the cloud, pipe, and devices?”
Increasing performance
  Increasing rate
  Increasing reliability
  Decreasing latency (delay)
  Increasing energy efficiency
  Decreasing cost
  …

## Slide 18: Course Approach 4/5
Two fundamental questions in wireless:
The second fundamental question, “What can we do with the achieved performance?”, will be touched upon briefly.
Applications in health care, intelligent transportation systems, energy network, …, through novel protocols, software, devices.

## Slide 19: Course Approach 5/5
Food for thought: Which question is more important?
Q1: “How can we increase the performance of wireless networks by efficient utilization of the cloud, pipe, and devices?”
Q2: “What can we do with the achieved performance?”

## Slide 20: Topics Covered 1/4
Actual coverage (as we progress) will be listed on the course web site.
Introduction
  Defining wireless
  Historic view
  Emerging issues
  dB notation
Propagation and Link Budget
  Antennas
  Pathloss in different wireless environments
  Large scale signal variation: Shadowing, reflection, diffraction, scattering, coverage
  Multipath and small scale signal variations
  Channel measurements and simulation
  Link budget

## Slide 21: Topics Covered 2/4
Cellular Communications
  Cellular communications principles
  Multiple access methods: FDMA, TDMA, CDMA, OFDM, random access
  Interference characterization
  Capacity, outage
  Macrocell, microcell, picocell, radio-over-fiber, distributed antennas
  1G, 2G, 3G, 4G, 5G cellular networks
Wireless Channel Characterization
  Multipath fading
  Coherence time, Doppler spread
  Coherence bandwidth, power delay profile

## Slide 22: Topics Covered 3/4
Digital Modulation and Interference
  Spectral efficiency
  Digital modulation methods
  Error performance in interference and fading
Diversity and Adaptive Equalization
  Principles, types and performance of diversity combining
  Adaptive equalization techniques for combating multipath
Systems Issues
  Scheduling
  Call admission control
  Multiuser diversity
  Interference management
  Radio resource management
  Routing

## Slide 23: Topics Covered 4/4
Miscellaneous
  Non-terrestrial networks
  6G networks
  Sensor networks
  Cognitive radio
  Multihop/mesh/relay networks
  Cooperative communications
  WLAN (802.11)