## Slide 1: SYSC 5704 Elements of Computer Systems
Fall 2011
SYSC 5704: Elements of Computer Systems
1
Optimization to take advantage of hardware.
Notes: 1
Course Outline 1st.

## Slide 2: Objectives
Simple things to speed up your program.
  Optimize
  Watch procedure calls
  Code motion
  Strength reduction
  Common expression removal.

## Slide 3: Example Matrix Multiplication
Standard desktop computer, compiler, using optimization flags
Both implementations have exactly the same operations count (2n3)
What is going on?
160x
Triple loop
Best code
This code is
not obviously stupid

## Slide 4: How did they do it?
  Multiple threads (4x)
  Vector instructions (4x)
  Memory hierarchy and other optimizations (20x)
    Blocking or tiling, loop unrolling, array scalarization, instruction scheduling.
    More instruction level parallelism, better register usage, less L1/L2 cache misses, Less TLB misses.

## Slide 5: The effect of naive coding
One can lose from 10-100x performance or more!
  Algorithm (O(n2) vs O(logn)
  Coding style (too many procedure calls, reordering, unrolling.
  Algorithm structure (locality, instruction level parallelism).
  Data representation.
This is why we need to understand computer architecture!

## Slide 6: Hint 1 : Use the optimizer!
Compiled without flags: ~1300 cycles
Compiled with –O3 –m64 -march=… –fno-tree-vectorize ~150 cycles
Core 2 Duo, 2.66 GHz
double a[4][4];
double b[4][4];
double c[4][4]; # set to zero
/* Multiply 4 x 4 matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < 4; i++)
for (j = 0; j < 4; j++)
for (k = 0; k < 4; k++)
c[i*4+j] += a[i*4 + k]*b[k*4 + j];
}

## Slide 7: Roadblocks
The compiler is conservative.
Aliasing (pointers) causes troubles.
Whole program optimization is too expensive.

## Slide 8: Hint 2 : Procedure calls
Small procedures are better for software engineering, but can be costly.
  Costs go way up if the procedure checks its arguments.
  Check bounds outside of loop, and design by contract.
In-line!

## Slide 9: Hint 3 : Code Motion
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}
Reduce frequency with which computation is performed
If it will always produce same result
Especially moving code out of loop
Sometimes also called precomputation or hoisting.
long j;
int ni = n*i;
for (j = 0; j < n; j++)
a[ni+j] = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 10: Even worse example!
Strlen loops until it finds a null, so we call this over and over again!
Move call to strlen outside of loop since result does not change from one iteration to another
What about 'A' - 'a'?
void lower(char *s)
{
int i;
int len = strlen(s);
for (i = 0; i < len; i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}
void lower(char *s)
{
int i;
for (i = 0; i < strlen(s); i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 11: Performance
  Time quadruples when string length is double - Quadratic performance
  Hoisting results in linear performance.
CPU Seconds (log scale)
String Length (log scale)
Chart: 
| 256 | 512 | 1k | 2k | 4k | 8k | 16k | 32k | 64k | 128k | 256k
lower1 | 0.000266 | 0.001033 | 0.004066 | 0.016678 | 0.067395 | 0.27087 | 1.0825 | 4.9645 | 20.0633 | 80.1428 | 341.5956
lower2 | 6e-06 | 1.2e-05 | 2.4e-05 | 4.8e-05 | 9.5e-05 | 0.000191 | 0.000382 | 0.000808 | 0.001615 | 0.003229 | 0.006694

## Slide 12: Hint 4 : Strength Reduction
Replace costly operation with simpler one
Example: Shift/add instead of multiply or divide
16*x → x << 4
Utility machine dependent
Depends on cost of multiply or divide instruction
On Pentium IV, integer multiply requires 10 CPU cycles
Example: Recognize sequence of products
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
a[n*i + j] = b[j];
int ni = 0;
for (i = 0; i < n; i++) {
for (j = 0; j < n; j++)
a[ni + j] = b[j];
ni += n;
}

## Slide 13: Hint 5 : Share Common Subexpressions
Reuse portions of expressions (factoring!)
Compilers often not very sophisticated in exploiting arithmetic properties
/* Sum neighbors of i,j */
up = val[(i-1)*n + j ];
down = val[(i+1)*n + j ];
left = val[i*n + j-1];
right = val[i*n + j+1];
sum = up + down + left + right;
int inj = i*n + j;
up = val[inj - n];
down = val[inj + n];
left = val[inj - 1];
right = val[inj + 1];
sum = up + down + left + right;
3 mults: i*n, (i–1)*n, (i+1)*n
1 mult: i*n