## Slide 1
Q(λ)-Learning Fuzzy Controller for the Homicidal Chauffeur Differential Game
Presented by: Prof. Howard M. Schwartz
Badr M. Al Faiya
20th Mediterranean Conference on Control and Automation - MED 2012
Barcelona, Spain
Department of Systems and Computer Engineering,
Carleton University, Ottawa, Canada

## Slide 2: Outline
Why training the evader in pursuit-evasion differential game
Why Q-learning fuzzy inference system (QLFIS)
Objective
Previous Work
Problem statement
Proposed solutions
Training the evader in pursuit-evasion differential games using QLFIS
Conclusions

## Slide 3: Why Training the Evader in Pursuit-Evasion Differential Game?
  The work done in the literature neither trained the evader to escape nor considered the capture condition
The solution is available
  evaluate the results
It can be used as a general problem for many other problems and real world applications
  missile avoidance
  collision avoidance (aircraft and mobile robots)
  obstacle avoidance

## Slide 4: Why Q-learning fuzzy inference system (QLFIS)
Fuzzy system
  Alternative way to replace conventional control
    Can deal with uncertainty in the environment
    Does not require a mathematical model
    Easy to modify rules using linguistic terms
  In robotics applications, for example
    Complexity of the environment makes it difficult to use pre-programmed robots

## Slide 5: Why Q-learning fuzzy inference system (QLFIS)
Reinforcement Learning (RL)
  Enables an agent (robot) to learn autonomously from its own experience by interacting with the real world (environment)
  Learning can find solutions that cannot be found in advance
      Environment or robot too complex
      Problem not fully known beforehand

## Slide 6: Homicidal Chauffeur Game
Homicidal Chauffeur Game
  The pursuer is a car-like mobile robot
  The evader (pedestrian) is a point
  that can move in any direction instantaneously
(1)
Equations of motion for the mobile robots are

## Slide 7: Objective
Design a highly maneuverable evader that can autonomously learn to escape from a pursuer in pursuit-evasion differential games

## Slide 8: RL For Robot Control
  The goal for the robot is to maximize the received rewards to find its best control actions
Design two fuzzy logic controllers that make a pursuer and an evader perform optimally
Fuzzy controller (FLC) is adapted by the RL algorithm
  Learning by interacting with the system

## Slide 9: Previous Work
Q(λ)-learning fuzzy logic controller for a multi-robot system(S. Desouky and H. Schwartz, SMC 2010)
  Train the pursuer to capture the evader and minimize the time of capture
An Experimental Adaptive Fuzzy Controller for Differential Games (S. Givigi and H. Schwartz, SMC 2009)
  A robot is pursuing another robot moving along a straight line

## Slide 10: The Problem
Lack of studies on how the evader can learn its optimal strategy

## Slide 11: Proposed Solutions
  Add the distance and the angle difference as inputs to the FLC of the evader
  The distance is critical for the evader when the pursuer approaches the evader to make a sharp turns to inter into Rp
  Apply QLFIS algorithm to train both the pursuer and the evader simultaneously
  Tune the input and the output parameters of the FLC

## Slide 12: Proposed Solutions
Analyze the game for the evader
  Investigate for the escape condition and the optimal solution
    Set the parameters to meet the escape condition
(3)
(4)
(2)

## Slide 13: Proposed Solutions
  So this is the ideal, our goal is to see if the learning algorithm will converge to the known optimal solution and train the evader to escape

## Slide 14: QLFIS Algorithm
ξ= [K c  ] are the parameters to be tuned
Qt+1(st,at) =Qt(st,at)+  t (et)
t = rt+1 +max Qt(st+1,a) Qt(st,at)
Update rules:
ξFIS(t +1) = ξFIS(t) + η t [∂Qt(st,ut)/∂ξFIS +   et−1 ]
ξFLC(t +1) =ξFLC(t)+  t [(∂u(st,ut)/∂ξFLC) (un-u/ σn)]
⊤

## Slide 15: Apply QLFIS Algorithm
Homicidal Chauffeur Game
  Pursuer learns to capture the evader and minimize the time of capture
  Evader learns to escape and maximize the time of capture, and learns the distance when to make sharp turns and avoid being captured

## Slide 16: Results
  We have set the game parameters such that it meets the escape condition given by Isaacs
  In theory the evader should be able to escape
  Fuzzy controller parameters initialization
  The pursuer captures the evader before learning to see how long it takes for the evader to learn how to escape
The players are then trained by tuning the input and output parameters of the fuzzy controller using QLFIS algorithm.

## Slide 17: Before Learning
Paths of the evader and the pursuer at the begining of learning

## Slide 18: Homicidal Chauffeur Game After Learning
 | no. of episodes | Capture time Tc (sec)
After learning using QLFIS | 100 | 12.90
 | 500 | 25.10
 | 900 | escape ( >60 sec )

## Slide 19: Conclusion
Reinforcement learning is used to train players in differential games.
The evader and the pursuer are trained by tuning the input and output parameters of a fuzzy controller using QLFIS algorithm.
We showed that the proposed technique trained the evader to escape from the pursuer after approximately 900 learning episodes

## Slide 20
Thank you