## Slide 1: Q(λ)-Learning Fuzzy Controller for the Homicidal Chauffeur Differential Game
Presented by: Prof. Howard M. Schwartz
Badr M. Al Faiya
Department of Systems and Computer Engineering,
Carleton University, Ottawa, Canada
20th Mediterranean Conference on Control and Automation - MED 2012
Barcelona, Spain
Wednesday, July 4

## Slide 2: Presentation Outline
  Objective
  Learning Algorithms
  Grid Games
  Differential Evader Pursuit Game
  Fuzzy Inference System
  Control Structure
  The Q(λ) Learning Fuzzy Controller Structure
  Results

## Slide 3: Objective
To create robots that can learn to work together either as part of a team or as competing teams. The goal is to develop learning algorithms for low cost simple robots and autonomous vehicles.
Applications in security and border protection, mapping, etc.
We are using two games to evaluate the algorithms they are:
  The evader pursuit game.
  The defending a territory game.

## Slide 4: Objective Cont.
Homicidal Chauffeur Game
  The pursuer is a car-like mobile robot
  The evader (pedestrian) is a point
  that can move in any direction
  Equations of motion for the mobile robots are

## Slide 5: Reinforcement Learning (RL)
  Enables an agent (robot) to learn autonomously from its own experience by interacting with the real world (environment)
  Learning can find solutions that cannot be found in advance
      Environment or robot too complex
      Problem not fully known beforehand

## Slide 6: The Q-Learning Algorithm (Reinforcement Learning)
Typically one either has Matrix Games (Stage Games) or Stochastic Games (Markov Games).
Matrix Games – Matching Pennies, Rock/Paper/Scissors, Prisoners’ Dilemma.
Grid Games

## Slide 7: The Value Functions
The value of a state s, is the expected future return of following policy π(s; a), starting from s can be written as,
We also define the action value function for a policy or a strategy,
The term is a little different from . The term
is the expected return if we choose action a, in state s and then follow
policy or strategy π afterwards.

## Slide 8: The Nominal Q-Learning Algorithm
Choose action a based on ε – greedy policy, move to next state s’, and receive reward r. Choose next action, a’ in state s’, then update Q table as,
You may also see this in the form,
We set α = 0.1 and γ = 0.9, these are typical values.
The performance difference between the above two implementations is minor.

## Slide 9: The Value of the Optimal Strategy

## Slide 10: Continuous Differential Game
We do not have discrete states and actions. We use Fuzzy logic controller to estimate the Action value function and the to determine the control action.
The Fuzzy Rules

## Slide 11: Analysis of the Game
Analyze the game for the evader
  Investigate for the escape condition and the optimal solution
    Set the parameters to meet the escape condition, l is capture radius, Rp is turning radius.
  Where γ = ratio of evader speed to pursuer speed

## Slide 12: The Actor/Critique Control Structure

## Slide 13: Some Membership Functions
A rule takes the form:
The output is the steering angle computed as,
Gaussian MF

## Slide 14: The Table of Rules
Φ | N | Z | P
N | -0.5 | -0.25 | 0.0
Z | -0.25 | 0.0 | 0.25
P | 0.0 | 0.25 | 0.5
 | N | Z | P
N | -0.5 | -0.25 | 0.0
Z | -0.25 | 0.0 | 0.25
P | 0.0 | 0.25 | 0.5
The pursuer’s fuzzy decision table and the output constant, before learning.
Φ d | VC | CS | FA
N | -π/2 | -π/2 | -π/4
Z | -π/2 | π/2 | 0.0
P | π/2 | π/2 | -π/4
Where, N-negative, Z-zero, P-positive, VC-very close, CS-close, FA-far
The evader’s fuzzy decision table and the output constant efore learning

## Slide 15: Apply QLFIS Algorithm
Homicidal Chauffeur Game
  Pursuer learns to capture the evader and minimize the time of capture
  Evader learns to escape and maximize the time of capture, and learns the distance when to make sharp turns and avoid being captured

## Slide 16: Simulation Initialization
  We have set the game parameters such that it meets the escape condition given by Isaacs
  In theory the evader should be able to escape
  Fuzzy controller parameters initialization
  The pursuer captures the evader before learning to see how long it takes for the evader to learn how to escape
The players are then trained by tuning the input and output parameters of the fuzzy controller using QLFIS algorithm.

## Slide 17: The Reward,
The pursuer wants to minimize the distance the evader wants to maximize the distance. We compute change in distance between pursuer and evader as,
The reward becomes
For Pursuer
For Evader

## Slide 18: The Learning Algorithm

## Slide 19: Before Learning

## Slide 20: Video of the Pursuit
100 training episodes
500 training episodes

## Slide 21: The Evader Gets Smarter
900 training episodes

## Slide 22: Our Experimental Work
Red Pursues Blue

## Slide 23: Conclusions and Future Work
Reinforcement learning is used to train players in differential games.
The evader and the pursuer are trained by tuning the input and output parameters of a fuzzy controller using QLFIS algorithm.
We showed that the proposed technique trained the evader to escape from the pursuer after approximately 900 learning episodes
We would like to dramatically decrease the learning time.
Need balance between Nurture versus Nature.