# Chapter 5

# Summary, Contributions and Future Work

5.1 Summary and conclusions

This research is an attempt to apply the cell-based method to construction simulation, trying to incorporate site layout planning, simulation and animation, to detect and resolve spatial conflicts, and to analyze the effects of spatial constraints.

The literature review of the construction simulation tools, the site layout planning approaches as well as the animation techniques has revealed some improved implementations in this field. During the past three decades, these tools opened the door for the construction simulation research and pushed it forward constantly. Nevertheless, the fact that workspace was not considered and spatial conflicts were not detected/resolved in construction simulation limited the application of these tools. Explicit representation of space will contribute to a more realistic simulation result. In addition, an adequate space representation can bridge the gap between site layout planning and simulation, allowing examination of the various site layout patterns in simulation. Moreover, a conflict-free and uninterrupted animation, which is helpful in site layout planning and visualizing the activity sequence, may be achieved by introducing the space into construction simulation.

This research proposed a cell-based construction simulation method using the Cell-DEVS technique. In this method, the spatial constraints, site layout patterns and resource allocations can be explicitly represented. Consequently, spatial conflicts can be detected and resolved. The effects of spatial constraints can be analyzed based on site layout patterns, resource combinations and changeable moving speeds. Two case studies were used to implement and demonstrate the advantages and applicability of this method.

The discussions and comparisons in this research demonstrate some distinguishing characteristics of the cell-based simulation method:

- It is a general-purpose simulation tool for broad domains and can be used to simulate complex construction operations, especially when spatial constraints are crucial to the project.

- Space is represented explicitly so that the occupation of the workspace and other spatial information about the construction environment can be understood more easily than the abstract symbols in simulation networks.

- Physical construction resources can be allocated considering different site layout patterns as if the user were planning a real project.

- The programmability and the capability of defining rules to control entities make the cell-based simulation systems more flexible and capable of detecting and resolving spatial conflicts during the simulation.

- An uninterrupted conflict-free animation provides a better means for the practitioners to check the simulation results and compare various resolutions.

- More information (occupancy, moving direction and ID, etc.) is integrated in the cell-based model, which makes it easy to identify and trace a specific object.  Furthermore, the detailed output helps to verify the outcome of the system.

- Space can be considered as an independent construction resource.

5.2 Contributions

The contributions of this research are grouped into the following areas:

- It is the first time to propose a construction simulation method which integrates site layout planning, simulation and animation. This cell-based, space-involved and conflict-resolving simulation method will help the decision makers or the field personnel to easily understand, predict and compare the performances of construction operations with different resource combinations considering site layout patterns. This innovative simulation method provides multiple perspectives to examine the construction operations in which space is explicitly represented and serves as an independent construction resource.

- Designed a general process to apply the cell-based method to the construction simulation. It consists of the Pre-processing, Main-processing and Post-processing phases, involving system modeling, preparing data input, simulation running, verification and validation, animation and result analysis. Through the three phases, a whole cell-based simulation system can be developed and implemented.

- Applied two case studies to demonstrate the advantages and applicability of the proposed method. A new cell-based model was developed for the case study of the Jacques Cartier Bridge rehabilitation project to consider different site layouts and investigate the effects of spatial constraints. This model overcame the limitations of the previous study. It took into account all necessary construction resources and used a group of cells to represent objects. Through a mechanism designed for the trucks to find their corresponding teams, different site layout patterns could be compared. The improvement in this research makes the model more practical and closer to the real conditions of the construction operations. The case study of the traffic flow analysis considering work zones presented a non-cyclic simulation system. Through the evaluation of the conditions on the observed road section and the control of the vehicles’ movement, the effects of construction operations on the traffic flow under different scenarios were investigated.

- Defined sets of rules for the Cell-DEVS models and related DEVS models to establish basic modules of the “Modeling Elements Library” that can be reused in the future. More than 500 rules are coded to control the movement of objects and explore the possibilities of detecting and resolving spatial conflicts. These rules have been tested over 200 successful tests for different resource combinations and site layout patterns. Based on the experience, the modeling concepts of “master-slave” cells and the “macros” were created, which greatly reduce the efforts of developing rules.

- Analyzed the simulation results according to different requirements. The effects of spatial constraints were quantified and the results were analyzed from the aspects of site layout patterns, resource combinations and the changeable moving speed. The simulation result shows that: (1) Pattern-A has less spatial constraints than the other two patterns; (2) The productivities of the cell-based method are lower than those of MicroCYCLONE by 3-5% (1-2 panels) when the object’s moving speed was constant; and (3) When the turning speed dropped from 10 km/h to 1km/h, the productivity might drop over 10% for some resource combinations (Figure 4.23). Through the comparisons with those of MicroCYCLONE, the results of the cell-based method reflect the effects of the spatial constraints. This difference illustrates that in some cases the impact of spatial constraints is significant and should not be neglected.

Although the manner and degree to which spatial constraints affect the construction operations may be different from one project to another, the perspectives to analyze simulation results provided in this chapter could be used for other projects to analyze the impact of spatio-temporal constraints.

5.3 Limitations and future work

While pursuing this research, several limitations have been identified related to the requirements and the performance of the developed method. In order to enhance the capabilities of the cell-based simulation method, the following points should be explored in the future research.

- More case studies should be investigated to further validate this cell-based method, and to accumulate more experiences in building models and developing rules, making this method more practical and easier for more applications.

- In the cell-based method, the simulator needs to scan each rule and related cells to check their activation conditions. When the amount of rules or cells is very large and the compositions of the entities such as resources and logical dependencies to start activities are complex, the simulation will become slow. A solution is Parallel CD++ (Glinsky and Wainer 2006; Liu and Wainer 2007). Using this parallel computing algorithm, the performance of the cell-based method can considerably speed up by distributing calculation over multiple possessors.

- More issues, such as site layout patterns and the size of cells, have to be considered in the proposed method. With the increase of the amount of entities, modeling may become complicated. A graphical modeling interface or other techniques that can facilitate modeling and data input should be developed.

- Based on the DEVSView (Khan et al. 2005), a 3D animation could be realized. On the other hand, since the cell-based simulation method provides a very detailed data output, the potential to link VITASCOPE could be also investigated.

References

AbouRizk, S.M., Ruwanpura, J.Y., Er, K.C., and Fernando, S. (1999). Special Purpose Simulation Template for Utility Tunnel Construction, Proceedings of the 1999 Winter Simulation Conference, pp. 948-955.

Ahmad, S., and Simonovic, S.P. (2004). Spatial System Dynamics: New Approach for Simulation of Water Resources Systems, Journal of Computing in Civil Engineering, ASCE, Vol. 18, No. 4, pp. 331-340.

Anumba, C., and Bishop, G. (1997). Importance of Safety Considerations in Site Layout and Organization.” Canadian Journal of Civil Engineering, Vol. 24 No. 2, pp. 229–236.

Balci, O. (1988). The Implementation of Four Conceptual Frameworks for Simulation Modeling in High-level Languages, Proceedings of the 1988 Winter Simulation Conference, San Diego, California, pp. 287-295.

Banks, J., and Carson, J.S. (1984). Discrete-Event System Simulation, Prentice-Hall, Inc., New Jersey.

Booch, G. (1991). Object Oriented Design with Applications, Benjamin/Cummings Publishing Company, Inc., Redwood City, California.

Caron, F., Marchet, G. and Perego, A. (2000). Layout Design in Manual Picking Systems: A Simulation Approach, Integrated Manufacturing Systems, Vol. 11No. 2, pp. 94-104.

Chang, D. Y., and Carr, R. I. (1987). RESQUE: A Resource Oriented Simulation System for multiple Resource Constrained  Processes, Proceedings of the PMI Seminar / Symposium, Milwaukee, Wisconsin, pp. 4-19.

Cheng, M.Y, and Yang, S.C. (2001). GIS-Based Cost Estimates Integrating with Material Layout Planning, Journal of Construction Engineering and Management, ASCE, Vol. 127, No. 4, pp. 291-299.

Cor, H. (1998). Using Simulation to Quantify the Impacts of Changes in Construction Work, Master thesis, Virginia Polytechnic Institute and State University, Blacksburg, Virginia.

Davidson, A. and Wainer, G. (2006). ATLAS: a Specification Language for Traffic Modelling and Simulation, Simulation, Practice and Experience, Elsevier. Vol. 14, No. 3, pp. 317-337.

Dawood, N., and Marasini, R. (2001). Stockyard Layout Management for Precast Concrete Products Using Simulation, Proceedings of CIB-W78 International Concrete Conference, IT in Construction in Africa, Mpumalanga, South Africa, Vol. 26, pp. 1-13.

Elbeltagi, E., Hegazy, T., and Eldosouky, A. (2004). Dynamic Layout of Construction Temporary Facilities Considering Safety, Journal of Construction Engineering and Management, ASCE, Vol. 130, No. 4, pp. 534-541.

El-Rayes, K. and Khalafallah, A. (2005). Trade-off between Safety and Cost in Planning Construction Site Layout, Journal of Construction Engineering and Management, ASCE, Vol. 131, No. 11, pp. 1186-1195.

Giambiasi, N. and Wainer, G. (2005) Cell-DEVS/GDEVS for Complex Continuous Systems. SIMULATION: Transactions of the Society for Modeling and Simulation International, Vol. 81, No. 2, pp.  137-151.

Gonzalez-Quevedo, A. A., AbouRizk, S. M., Iseley, D. T., and Halpin, D. W. (2002). Comparison of Two Simulation Methodologies in Construction, Journal of Construction Engineering and Management, ASCE, Vol. 119, No. 3, pp. 573-589.

Guo, S. (2002). Identification and Resolution of Workspace Conflicts in Building Construction, Journal of Construction Engineering and Management, ASCE, Vol. 128, No. 4, pp. 287-295.

Glinsky, E. and Wainer, G. (2006). New Parallel simulation techniques of DEVS and Cell-DEVS in CD++, Proceedings of the 38th IEEE/SCS Annual Simulation Symposium, Huntsville, AL. 2006.

Hajjar, D., and AbouRizk, S.M. (1998). Modeling and Analysis of Aggregate Production Operations, Journal of Construction Engineering and Management, ASCE, Vol. 124, No. 5, pp. 390-401.

Hajjar, D., and AbouRizk, S.M. (1999). Simphony: an Environment for Building Special Purpose Construction Simulation Tools, Proceedings of the 1999 Winter Simulation Conference, pp. 998-1006.

Hajjar, D., and AbouRizk, S.M. (2002). Unified Modeling Methodology for Construction Simulation, Journal of Construction Engineering and Management, ASCE, Vol. 128, No. 2, pp. 174-185.

Halpin, D.W. (1973). An Investigation of the Use of Simulation Networks for Modeling Construction Operations, PhD dissertation, University of Illinois at Urbana-Champain, Illinois.

Halpin, D.W. (1977). CYCLONE: Method for Modeling of Job Site Processes, Journal of the Construction Division, ASCE, Vol. 103, No. 3, pp. 489-499.

Halpin, D.W., and Riggs, L.S. (1992). Planning and Analysis of Construction Operations, Wiley Interscience, New York, 1992.

Hamiani, A. (1989). Knowledge Representation for the Site Layout Problem, Proceedings of the 6th Conference on Computing in Civil Engineering, New York, pp. 283-289.

Harmanani, H., Zouein, P., and Hajar, A. (2000). An Evolutionary Algorithm for Solving the Geometrically Constrained Site Layout Problem, Proceedings of  8th ASCE International Conference on Computing in Civil and Building Engineering, (ICCCBE-VIII), Stanford University, 1442–1449.

Hegazy, T. M., and Elbeltagi, E. (1999). EvoSite: Evolution-Based Model for Site Layout Planning, Journal of Computing in Civil Engineering, Vol. 13, No. 3, pp. 198-206.

Henriksen, J. O. (1998). Window-based Animation with PROOF, Proceedings of the 1998 Winter Simulation Conference, San, Diego, California,  pp. 241-247.

Hooper, J. W. (1986). Strategy Related Characteristics of Discrete-event Languages and Models, Simulation, Vol. 46, No. 4, pp. 153-159.

Huang, R. Y., and Halpin, D. W. (1994). Graphical-based Method for Transient Evaluation of Constructin Operations, Journal of Construction Engineering and Management, ASCE, Vol. 121, No. 2, pp. 222-229.

Ioannou, P. G., and Martinez, J. C. (1996). Animation of Complex Construction Simulation Models, Proceedings of 3rd Congress on Computing in Civil Engineering, ASCE,  Reston, VA, pp. 620-626.

Ioannou, P. G., and Martinez, J. C. (1996a). Comparison of Construction Alternatives Using Matched Simulation Experiments, Journal of Construction Engineering and Management, ASCE, Vol. 122, No. 3, pp. 222-229.

Islier, A. A. (1998). A Genetic Algorithm Approach for Multiple Criteria Facility Layout Design, International Journal of Production Research, Vol. 36, No. 6, 1549-1569.

Jen, H. (2005). Web-based Construction Process Simulation Framework, Doctoral dissertation, School of Civil Engineering, Purdue University, W. Lafayette, Indiana.

Kamat, V. R., and Martinez, J. C. (2001). Visualizing Simulated Construction Operations in 3D, Journal of Computing in Civil Engineering, ASCE, Vol. 15, No. 4, pp. 329-337.

Kamat, V. R. (2003). VITASCOPE – Extensible and Scalable 3D Visualization of Simulated Construction Operations, Doctoral dissertation, Department of Civil Engineering, Virginia Polytechnic Institute and State University, Blacksburg, Virginia.

Kamat, V.R., and Martinez, J.C. (2004). Practical 3D Animation of Multiply Articulated Construction Equipment, Proceedings of the 2004 Winter Simulation Conference, pp.1229-1237.

Kamat, V.R., and Martinez, J. C. (2006). Interactive Collision Detection in Three-Dimensional Visualizations of Simulated Construction Operations, Engineering with Computers, Springer, London, UK.

Khan, A., Venhola, W., Wainer, G. and Jemtrud. M. (2005). Advanced DEVS Model Visualization. Proceedings of  IMACS World Congress on Scientific Computation, Applied Mathematics and Simulation 2005, Paris, France. 2005. VI.

Khoury, H. M., Kamat V. R., and Ioannou P. G. (2006). Simulation and Visualization of  Air-side Operations at Detroit  Metropolitan Airport, Proceedings of 2006 Winter Simulation Conference, Monterey, California, pp. 2029-2038.

Kumara, S. R. T., Kashyap, R. L., and Moodie, C. L. (1988). Application of Expert Systems and Pattern Recognition Methodologies to Facilities Layout Planning, International Journal Production Research, Vol. 26, No. 5, pp. 905-930.

Lee, E. B., Harvey, J. T., and Thomas, D. (2005a). Integrated Design / Construction / Operations Analysis for Fast-Track Urban Freeway Reconstruction, Journal of Construction Engineering and Management, ASCE, Vol. 131, No. 12, pp. 1283-1291.

Lee, E. B., and Ibbs, C. W. (2005b). Computer Simulation Model: Construction analysis for Pavement Rehabilitation Strategies, Journal of Construction Engineering and Management, ASCE, Vol. 131, No. 4, pp. 449-458.

Lee, E. B., Thomas, D., and Bloomberg, L. (2005b). Planning Urban Highway Reconstruction with Traffic Demand Affected construction Schedule, Journal of Construction Engineering and Management, ASCE, Vol. 131, No. 10, pp. 752-761.

Li, H., and Love, P.E.D. (1998). Site-level Facilities Layout Using Genetic Algorithms, Journal of Computing in Civil Engineering, ASCE, Vol. 12, No. 4, pp. 227-231.

Liu, L. Y. and Ioannou, P.G. (1992). Graphical Object-Oriented Simulation System for Construction Process Modeling, Proceedings of the Eighth Conference on Computing in Civil Engineering, ASCE, Dallas, Texas, pp. 1139-1146.

Liu, Q. and Wainer, G. (2007) Improving CD++ Parallel Simulation Engine, Proceedings of the 39th IEEE/SCS Annual Simulation Symposium. Norfolk, VA, USA. 2007.

Lluch, J. F., and Halpin, D. W. (1981). Analysis of Construction Operations Using Microcomputers, Journal of the Construction Division, ASCE, Vol. 108, No. CO1, pp. 129-145.

Lutz, J. D., Halpin, D. W., and Wilson, J. R. (1994). Simulation of Learning Development in Repetitive Construction. Journal of Construction Engineering and Management, ASCE, Vol. 120, No. 4, pp. 753-773.

Madhoun, R., and Wainer, G. (2007). Studying the Impact of Web-Services Implementation of Distributed Simulation of DEVS and Cell-DEVS Models, Proceedings of 2007 DEVS Integrative M&S Symposium (DEVS'07), Norfolk, Virginia, USA.

Marasini, R., and Dawood, N. (2002). Simulation Modeling and Optimization of Stockyard Layout for Precast Concrete Products, Proceedings of the 2002 Winter Simulation Conference, pp. 1731-1736.

Martinez, J.C. and P.G. Ioannou (1994). General Purpose Simulation with Stroboscope, Proceedings of the 2004 Winter Simulation Conference, Lake Buena Vista, Florida, pp. 1159-1166.

Martinez, J. C., and Ioannou, P. G. (1995). Advantages of the Activity Scanning Approach in the Modeling of Complex Construction Processes, Proceedings of 1995 Winter Simulation Conference, San Diego, California, pp. 1024-1031.

Martinez, J. C. (1996). STROBOSCOPE: State and Resource Based Simulation of Construction Processes, Doctoral dissertation, University of Michigan, Ann Arbor, Michigan.

Martinez, J.C. (1998). EarthMover – Simulation Tool for Earthwork Planning, Proceedings of the 1998 CIB W78 Conference, Department of Construction Management and Economics, Royal Institute of Technology, Stockholm, Sweden.

Martinez, J. C., and Ioannou, P. (1999). General–purpose Systems for Effective Construction Simulation, Journal of Construction Engineering and Management, ASCE, Vol. 125, No. 4, pp. 265-276.

Marzouk, M. and Moselhi, O. (2003). Object-Oriented Simulation Model for Earthmoving Operations, Journal of Construction Engineering and Management, ASCE, Vol. 129, No. 2, pp. 173-181.

Mawdesley, M.J., Al-jibouri, S.H., and Yang H. (2002). Genetic Algorithms for Construction Site Layout in Project Planning, Journal of Construction Engineering and Management, ASCE, Vol. 128, No. 5, pp. 418-426.

Muzy, A., E. Innocenti, A. A, Santucci, J. F., Santoni, P. and Hill, D. (2005) Modelling and Simulation of Ecological Propagation Processes: Application to Fire Spread, Environmental Modeling and Software, Vol. 20, pp. 827-42.

Naji, K. K. (1997). The Development of A Virtual Environment for Simulating Equipment-based Operations in Real-time Object-oriented Systems, Doctoral dissertation, University of Florida, Gainesville, Florida.

Nassar, K., Thabet, W., and Beliveau, Y. (2003). Simulation of Asphalt Paving Operations under Lane Closure Conditions, Automation in Construction, Vol. 12, pp. 527-541.

Odeh, A. M., Tommelein I. D., and Carr R. I. (1992). Knowledge-based Simulation of Construction Plans,  Proceedings of the Eighth Conference on Computing in Civil Engineering, ASCE, Dallas, Texas, pp. 1042-1049.

Oloufa, A. A. (1992). Feedback Mechanisms for Operational Simulation, Journal of Computing in Civil Engineering, ASCE, Vol. 6, No. 2, pp. 161-177.

Oloufa, A. A. (1993). Modeling Operational Activities in Object-Oriented Simulation, Journal of Computing in Civil Engineering, ASCE, Vol. 7, No. 1, pp. 94-106.

Palaniappan, S., Sawhney, A. and Sarjoughian, H. S. (2006).  Application of the DEVS Framework in Construction Simulation, Proceedings of 2006 Winter Simulation Conference, Monterey, California, pp. 2077-2086.

Pang, H., Zhang, C., and Hammad, A. (2006). Sensitivity Analysis of Construction Simulation Using Cell-DEVS and MicroCYCLONE, Proceedings of 2006 Winter Simulation Conference, Monterey, California, pp. 2021-2028.

Pang, H., Zhang, C., and Hammad, A. (2007). Sensitivity Analysis of Construction Simulation Considering Site Layout Patterns, International Workshop on Computing in Civil Engineering, Pittsburgh, Pennsylvania, July 2007.

Paulson, B. C., Jr. (1987).  Interactive Graphics for Simulating Construction Operations, Journal of the Construction Division, ASCE, Vol. 104, No. 1, pp. 69-76.

Pidd, M. (1998). Computer Simulation in Management Science, Wiley, Chichester, U.K.

PJCCI 2004: The official website of Jacques Cartier and Champlain Bridges Incorporated [online]. Available from http://www.pjcci.ca/ [cited on August 18, 2004].

Randhawa, S.U. and Sharoff, R. (1995), Simulation Base Design Evaluation of Unit Load Automated Storage/ Retrieval Systems, Computers and Industrial Engineering, Vol. 28, No. 1, pp. 71-79.

Riley, D. R., and Sanvido, V. E. (1995). Patterns of Construction-Space Use in Multistory Buildings, Journal of Construction Engineering and Management, ASCE, Vol. 121, No. 4, pp. 464-473.

Riley, D. R., and Sanvido, V. E. (1997). Space Planning Method for Multistory Building Construction, Journal of Construction Engineering and Management, ASCE, Vol, 123, No. 2, pp. 171-180.

Shang, H. and Wainer, G. (2005). A Model of Virus Spreading Using Cell-DEVS, Proceedings of the International Conference on Computational Science, Atlanta, GA.

Shang, H. and Wainer, G. (2006). A Simulation Algorithm for Dynamic Structure DEVS Modeling, Proceedings of 2006 Winter Simulation Conference, Monterey, California, pp. 815-822.

Shi, J. (1999). Activity-based Construction (ABC) Modeling and Simulation Method, Journal of Construction Engineering and Management, ASCE, Vol, 125, No. 5, pp. 354-360.

Shi, J., and Zhang, H.(1999). Iconic Animation of Construction Simulation, Proceedings of the 1999 Winter Simulation Conference, Vol, 2, pp. 992-997.

Shi, J. (2000). Object-oriented Technology for Enhancing Activity-based Modeling Functionality, Proceedings of the 2000 Winter Simulation Conference, pp. 1938-1944.

Tam, C.M., Tong, T.K.L., and Chan, W.K.W. (2001). Genetic Algorithm for Optimizing Supply Locations around Tower Crane, Journal of Construction Engineering and Management, ASCE, Vol. 127, No. 4, pp. 315-321.

Tartaro, M.L., Torres, C., and Wainer, G. (2001). Defining Models of Urban Traffic Using the TSC Tool, Proceedings of the 2001 Winter Simulation Conference, Arlington, VA, USA, pp. 1056-1063.

Tawfik, H. M., and Fernando, T. (2001).  A Simulation Environment for Construction Site Planning, Proceedings of 5th International Conference, Information Visualization, London, U.K., pp. 199-204.

Thabet, W. Y., and Beliveau, Y. J. (1994). Modeling Work Space to Schedule Repetitive Floors in Multistory Buildings, Journal of Construction Engineering and Management, ASCE, Vol. 120, No. 1, pp. 96-116.

Tocher, K. T. (1963). The Art of Simulation, English Universities Press, London.

Tommelein, I. D., Levitt, R. E., and Hayes-Roth, B. (1992). Site-layout Modeling: How Can Artificial Intelligence Help? Journal of Construction Engineering and Management, ASCE, Vol. 118, No. 3, pp. 594-611.

Touran, A., and Asai, T. (1987). Simulation of Tunneling Operations, Journal of Construction Engineering and Management, ASCE, Vol. 113, No. 4, pp. 554-568.

Vanegas, J. A., and Halpin, D. W. (1993). Simulation Technologies for Planning Heavy Construction processes, Journal of Construction Engineering and Management, ASCE, Vol. 119, No. 2, pp. 336-354.

VITASCOPE 2003 [online]. Available from http://pathfinder.engin.umich.edu [cited on November 12, 2005].

Wainer, G. (1998). Discrete-events Cellular Models with Explicit Delays, Doctoral dissertation, Université d'Aix-Marseille III.

Wainer, G., and Giambiasi. N. (2001). Application of the Cell-DEVS Paradigm for Cell Spaces Modeling and Simulation, SIMULATION, Transactions of the SCS, Vol. 76, No. 1, pp. 22-39.

Wainer, G. (2002). CD++: a Toolkit to Define Discrete-event Models, Software, Practice and Experience, Wiley. Vol. 32, No.3, pp. 1261-1306.

Wainer, G., and Giambiasi, N. (2002). N-Dimensional Cell-DEVS, Discrete Events Systems: Theory and Applications, Kluwer. Vol. 12, No. 1, pp. 135-157.

Wainer, G. (2006). Applying Cell-DEVS Methodology for Modeling the Environment, SIMULATION, Transactions of the SCS, Vol. 82, No. 10, pp. 635-660.

Wandha, L.C. (2000), Optimizing Deployment of Shiploaders at Bulk Export Terminal, Journal of Waterway, Port, Coastal and Ocean Engineering , Nov/Dec, 2000, pp.297-304.

Wolfram, S. (1986). Theory and Application of Cellular Automata, Vol. 1, Advances Series on Complex Systems, World Scientific, Singapore.

Yeh, I.-C. (1995). Construction-site Layout Using Annealed Neural Network, Journal of Computing in Civil Engineering, ASCE, Vol. 9, No. 3, pp. 201-208.

Zaki, A. R., and Mailhot, G. (2003). Deck Reconstruction of Jacques Cartier Bridge Using Precast Prestressed High Performance Concrete Panels, PCI Journal.

Zayed, T. M. and Halpin, D. (2001). Simulation of Concrete Batch Plant Production, Journal of Construction Engineering and Management, ASCE, Vol. 127, No. 2, pp. 132-141.

Zeigler, B.P. (1976). Theory of Modelling and Simulation, Wiley-Interscience Publication.

Zhang, C., Hammad, A., Zayed, T.M., and Wainer, G., (2005). Representation and Analysis of Spatial Resources in construction Simulation, Proceedings of 2005 Winter Simulation Conference, Orlando, Florida,  pp. 1541-1548.

Zhang, C., Hammad, A., Zayed, T.M., Wainer, G., and Pang, H. (2007). Cell-based Representation and Analysis of Spatial Resources in Construction Simulation, Automation in Construction,  Vol. 16, No. 4, pp. 436-448.

Zhang, H., Shi, J.J., and Tam, C. M. (2002). Iconic Animation for Activity-based Construction Simulation, Journal of Computing in Civil Engineering, ASCE, Vol. 16, No. 3, pp. 157-164.

Zhang, H., Tam, C.M., and Li, H. (2005). Activity Object-Oriented Simulation Strategy for Modeling Construction Operations, Journal of Computing in Civil Engineering, ASCE, Vol. 19, No. 3, pp. 313-322.

Zhong, D., Li, J., Zhu, H., and Song, L. (2004). Geographic Information System-Based Visual Simulation Methodology and Its Application in Concrete Dam Construction Processes, Journal of Construction Engineering and Management, ASCE, Vol. 130, No. 5, pp. 742-750.

Zouein, P. P., and Tommelein, I. D. (1999). Dynamic Layout planning Using a Hybrid Incremental Solution Method, Journal of Construction Engineering and Management, ASCE, Vol. 125, No. 6, pp. 400-408.

Zouein, P. P., Harmanani, H. and Hajar, A. (2002). Genetic Algorithm for Solving Site Layout Problem with Unequal-Size and Constrained Facilities. Journal of Computing in Civil Engineering, ASCE, Vol. 16, No. 2, pp. 143-151.